FILE:  10m_sst.doc
AUTH:  R. Knuteson
       Space Science and Engineering Center
       U. Wisconsin - Madison
       1225 W. Dayton St, Madison, WI 53706
DATE:  4/11/96
RE:    CSP Cruise Data (10 micron filter)

The files 10M_S55.QC2 and 10M_W55.QC2 
contain the 55 degree angle AERI observations, for
the sky and water views respectively, for the
CSP TWP cruise period (15 Mar - 13 Apr 1996)
after application of a 10 micron spectral 
filter provided by P.M. appropriate for the
Heimann IRT cameras he is using.  The QC2
extension indicates that an initial quality control
step has been performed to remove spurious data
due to a warm detector or a tarp covering the
viewport of the instrument.  Null records due
to instrument restarts have also been removed.

The file 10M_SST.DAT contains the skin temperature
derived from the water and sky radiance
observations. Note that the correction for the
9 meter height of the instrument above the surface
has NOT been made in this PRELIMINARY DATA. 

Please do not reproduce or redistribute without
first contacting me to obtain the latest results:
robert.knuteson@ssec.wisc.edu (608-263-7974).

Directory of A:\10M

.            <DIR>      4-11-96   3:32p
..           <DIR>      4-11-96   3:32p
10M      DOC     1170   4-11-96   3:57p
10M_S55  QC2    96394   4-11-96   1:55a
10M_W55  QC2    96378   4-11-96   1:55a
10M_SST  DAT   104056   4-11-96   2:52a
        6 file(s)     297998 bytes used