Practical Session:

Remote Sensing and Wildfire Monitoring

The practical will consist of 3 sections:

- MODIS imagery of Cape Town fires

- Comparison between MODIS fire products and a Spot 2 scene

- Fire detection with AFIS II

Cape fires, December 2008 (Lab 1)

The fire that began in Grabow on  Saturday spread to the Gordon's Bay area by Monday and residents were evacuated. Many stood watching the 150 - 200 firefighters battling the blaze from below but several homes were damaged and at least 3 razed to the ground.

Task1:

Open ENVI 4.6 and load channel 1 and channel 2 (250m) MODIS corrected surface reflectance images as GeoTiff

Go to C:\IGARSS09\Fire\lab1

Task2:

Open MODIS channel 1 and channel 2 in a band 1:2:1 false colour composite and load RGB

Task 3:

Click in the scroll map on Cape Town and then use the Enhance option to do a 2% histogram stretch. A large fire will be visible east of Cape Town with a smoke plume drifting west

Task 4:

Continue by loading all 7 MODIS 500m images and evaluate the individual bands in relation to: (Rating bands from 0 – 5, 0 = poor, 5 = excellent)

- Their ability to characterise the Gordons bay fire scar

- Their ability to identify open flames (active fire pixels)

- Their ability to detect the smoke plume

Task 5:

Evaluate different combinations of bands in R G B and provide a combination that best describes:

- The fire scar

- Active Fire

- The smoke plume

MODIS bands

Landsat Bands

| Primary Use | Band | Bandwidth |
| --- | --- | --- |
| Land/Cloud Boundaries | 1 | 620-670 |
|  | 2 | 841-876 |
| Land/Cloud Properties | 3 | 459-479 |
|  | 4 | 545-565 |
|  | 5 | 1230-1250 |
|  | 6 | 1628-1652 |
|  | 7 | 2105-2155 |

| MODIS bands | Active fire | Burned Area | Smoke |
| --- | --- | --- | --- |
| Band 1 620-670 |  |  |  |
| Band 2 841-876 |  |  |  |
| Band 3 459-479 |  |  |  |
| Band 4 545-565 |  |  |  |
| Band 5 1230-1250 |  |  |  |
| Band 6 1628-1652 |  |  |  |
| Band 7 2105-2155 |  |  |  |

MODIS product evaluation (Lab 2)

Sabie forest fires 2007

The MODIS product evaluation aims to provide an overview of the current MODIS fire products.

Available data sets

C:/IGARSS09/Fire/lab2

- MODIS Corrected surface reflectance

(MOD/MYD 09) 27, 28 and 29 July 2007

- MODIS Active fires (MOD 14) July 2007

- MODIS Roy Burned area (MCD43) July 2007

- MODIS Louis Burned area July 2007

- Spot 2 high resolution image 11 Aug 2007

Step 1: Open days 27 – 29 July 2007 of MODIS MOD/MYD 09 data and find the forest fire in Sabie

Step 2: Open Spot 2 high resolution image in ENVI

Step 3: Use the ROI tool to map the burned area and create a shapefile

Step 4: Open ArcMap and add the Roy burned area map

Step 5: Open the active fire product

Step 6: Look at the differences between the two products for different fires

Question1: Why in some cases do the burn area product and active fire product agree on area affected and some not at all?

Step 7: Switch off the Roy burned area and load the Louis burned area product.

Question 2: Do one see the same picture?

Step 8: Switch off the active fire product and toggle between the Roy and Louis burned area products

Question 3: Why do you see differences?

Step 9: Open the Spot burned area layer on top of the Roy and Louis products and review the difference

AFIS viewer (Lab 3)

Lab 3 will involve the live tracking of the MODIS Aqua overpass at 14:13 pm.

Step 1:

Open WAMIS portal

www.wamis.co.za

Step 2:

Open AFIS