File: HISAE.DOC
Date: October 31, 1991
From: Ben Howell
To:   For the Record
Subject: The HIS Aircraft Experiment

     This document combines several other documentation files that I
have written and distributed, on a limited basis, to personnel working
within the Space Science and Engineering Center.  This is an effort to
consolidate, improve and augment the documentation so that
participants in the HIS aircraft experiments can have a reference
which defines the basic instrument parameters, outlines the necessary
steps in the data processing and describes the formats of the "final"
data products.
     There are six sections -- (only four included)

          1. Instrument Parameters
          2. Housekeeping Channels
          3. Data Processing
          4. Data File Formats

1. Instrument Parameters

     ----  ------- -------     -------     ------------  --   ----- ------
     BAND  CHANNEL    WNA         WNB      USEFUL RANGE  RF   NUSED  NTOTL
     ----  ------- -------     -------     ------------  --   ----- ------
     III       1   1974.875    2962.3125   2050 .. 2650   8   2048   4096
      II       2    987.4375   1974.875    1075 .. 1825   8   2700   4096
       I       3    564.25     1128.50      600 .. 1075  14   3500   4096
     ----  ------- -------     -------     ------------  --   ----- ------
     Definitions:
          SFMX -- maximum sampling frequency (15799.000)
          RF   -- reduction factor
          TSR  -- total spectral range (= SFMX/RF)
          DX   -- delay interval (= 1/TSR)
          NTOTL-- the maximum number of points per interferogram
          DWN  -- spectral interval (= 1/(NTOTL * DX) )
          NUSED-- typical number of interferogram points used in FFT
          SR   -- spectral resolution(= 1/(NUSED * DX) )
          WNA  -- minimum wavenumber (reciprocal cm.):
          WNB  -- maximum wavenumber (reciprocal cm.)
          (For channels 2 and 3, WNB = TSR, WNA=WNB*0.5, and
           for channel 1, WNA=TSR, WNB=WNA*1.5)

          2. Housekeeping channels -- The samples of the items listed below are
          found in each housekeeping record.  The program HKLOG (.EXE) extracts
          those items and writes them, preceded by source-file record number and
          time (floating point hour plus fraction), into two files.  The output
          files may be in either ASCII text or binary form.
               The first of the two files contains the following items, which
          are sampled every four seconds:
                1. BB READOUT SELECT FLAG
                2. COLD BB CONTROLLER ON/OFF FLAG
                3. HOT BB CONTROLLER ON/OFF FLAG
                4. AFT PILOT SWITCH ON/OFF FLAG
                5. AFT PILOT SWITCH STANDBY FLAG
                6. FWD PILOT SWITCH ON/OFF FLAG
                7. FWD PILOT SWITCH STANDBY FLAG
                8. ELECTRONIC HEATER ON/OFF FLAG
                9. ELECTRONIC HEATER EN/DIS FLAG
               10. SCAM DIP-SWITCH SW0 (SCENE MIRROR)
               11. SCAM DIP-SWITCH SW1 (INSTR.MODE)
               12. ASCENT DURATION TIME LIMIT
               13. ASCENT DUR. LIMIT EN/DIS
               14. WARMUP DURATION TIME LIMIT
               15. WARMUP DUR. LIMIT EN/DIS
               16. HOT BB TEMP. SETTING
               17. HOT BB CONTROLLER ON/OFF
               18. COLD BB TEMP. SETTING
               19. COLD BB CONTROLLER ON/OFF
               20. ELECTRONIC HEATER EN/DIS
               21. INTERFEROMETER SCAN SPEED
               22. INTERFEROMETER SCAN LENGTH
               23. SCENE MIRROR POSITION
               24. HOT BB SETPOINT
               25. HOT BB TEMPERATURE
               26. COLD BB SETPOINT
               27. COLD BB TEMPERATURE
               The second file contains the following items, which are sampled
          once per second:
                1. BEAMSPLITTER TEMPERATURE
                2. LASER TEMPERATURE
                3. APERTURE STOP TEMPERATURE
                4. SCAM ENCLOSURE TEMPERATURE
                5. RECORDER DRIVE TEMPERATURE
                6. POWER SUPPLY TEMPERATURE
                7. BOMEM POWER SUPPLY TEMPERATURE
                8. POD INSIDE AIR TEMPERATURE
                9. DEWAR WINDOW TEMPERATURE
               10. OPTICS MIRROR TEMPERATURE
               11. OPTICS BENCH TEMPERATURE
               12. BLACKBODY HEATSINK TEMPERATURE
               13. ATMOSPHERIC PRESSURE (MB)
               14. DETECTOR NO.1 OUTPUT DC LEVEL
               15. DETECTOR NO.2 OUTPUT DC LEVEL
               16. DETECTOR NO.3 OUTPUT DC LEVEL
               17. DEWAR TEMPERATURE NO.1 (K)
               18. DEWAR TEMPERATURE NO.2 (K)

3. Data Processing
               The data from the HIS are recorded on high-capacity (65MB)
          cassette tapes.  A single flight may generate 2 tapes of data, at a
          recording rate of about 240 kilobytes per minute of operation.  A note
          of CAUTION!! -- before starting a processing task, it is wise to check
          the amount of available disk space!  For each megabyte (MB) of raw
          data, the processed data files have the following approximate sizes:
          
                    Interferograms -- 1 MB
                    Complex, Uncalibrated Spectra -- 2 MB
                    Real, Calibrated Spectra -- 1 MB
          
          In addition to these files, there are a number of smaller text files,
          so it is advisable to have at least 5MB of available disk space for
          each MB or raw data.
               The processing of HIS data from the raw "3M" cassette to
          calibrated radiance spectra is described below, in a logical sequence,
          with the appropriate executable (.EXE) file indicated in capital
          letters.
          
               Using the IBM-AT computer connected to the 3M tape drive, change
          to the directory C:\HIS and run EATHIS.EXE to copy the desired data
          segment to disk.  Read the document "EATHIS.DOC" for details on
          running that program.  The raw data volume is about 240KB per minute
          of observation, one record being 1024 bytes with a recording rate of
          about 240 records per minute, so be sure there's enough disk space for
          the volume of data you plan to copy.  If a file server is operating,
          specify the output file to be in an appropriate directory on the
          server fixed disk, or on the magneto-optical disk.  For example, raw
          data from the flight of 1 Aug 91 would be written in the directory
          \AC080191\RAW.  The supporting file "DWRTFN.DAT" , which contains
          coefficients for the computation of dewar temperatures, must be in the
          default directory.
          
          NOTE:From here on, the programs described all run under OS/2.
          
               With the raw data on disk, the next step is to extract and file
          the housekeeping data for later examination.  On a PC connected to the
          file server, run the program HKLOG.EXE to write housekeeping data into
          three files which may then be examined by running the program
          HKVIEW.EXE.
               The assembling of interferograms for each of 3 channels and 2
          scan directions is the job of HISAC1.EXE.  Currently, the 6 files
          output from this program have names with the pattern "IFN", where "N"
          has the value from 1 to 6 representing:
          
                    N  Channel  Scan Direction
                    1     1       1
                    2     1       2
                    3     2       1
                    4     2       2
                    5     3       1
                    6     3       2
          

               The interferograms are then transformed into complex spectra
          using the program HISAC2.EXE.  Optional output includes files of the
          real and imaginary parts, magnitude and phase.  The optional outputs
          are usually selected only when performing quality control (QC) with a
          short time segment.
               The uncalibrated (complex) spectra are usually named "HSN", with
          "N" representing the index previously described.
          
               Calibrated radiance spectra are produced by HISAC3.EXE.  The
          primary output files are named "HCN", with the "N" representing the
          channel/scan direction combination, as described above.  These spectra
          may be considered the "standard" output product of the HIS data
          processing, but additional steps are necessary for certain
          applications.
          
               A useful addition to the files of calibrated spectra, i.e. the
          "HCN" files, is the aircraft information corresponding to the time of
          the HIS observations.  The program NAVHIS.EXE reads the appropriate
          aircraft navigation file and writes the aircraft data, i.e. latitude,
          longitude, altitude and heading into the header words of each record.
          
               For certain applications apodized spectra are desired.
          Apodization reduces the "ringing" effect of the finite Fourier
          transform.  The program APODIZE.EXE generates apodized spectra, by
          means of a double FFT.  The apodized spectra are usually appropriately
          named with an "A" added to the input file name, for example "HC6.ARS"
          is often used to name a file of "Apodized Radiance Spectra", hence
          "ARS".
          
               Averaging calibrated spectra over scan direction is accomplished
          by running the program AVDIRS.EXE.  The naming convention has been to
          output "HC1N2" for input files "HC1" and "HC2", "HC3N4", etc. and
          "HC5N6".
          
               THe program COADDHIS.EXE is used to compute averages of spectra
          over time (and thus distance).  Since the normal sequence of scene-
          mirror positions is
                    2 hot blackbody views
                    2 cold blacbody views
                    6 earth views
          the averaging of earth spectra is usually done over 6 spectra.  The
          files with the extension ".EAV" are averaged earth-view spectra.
          
               Use the program BTSPECMR.EXE to compute brightness-temperature
          spectra from radiance spectra.  The output file should be named in a
          way that it denotes a brightness temperature spectrum.
          
               Spectra generated by the previous steps, with the exception of
          the complex spectra, can be plotted using PLOVR.EXE.
          

               The time, scene-mirror position, blackbody temperatures as well
          as the aircraft latitude, longitude, altitude and heading for each
          interferogram or spectrum can be displayed using the program
          DISREC.EXE.  The items mentioned above are displayed if the option of
          a "fixed format" is selected.  If the "variable" option is selected,
          any of the 100 header words can be displayed for each record.
          
               If a portion of a large file of spectra is desired, use the
          program GETRECS.EXE to extract the desired records and write a new,
          smaller file.
          
               The program APPFILES.EXE can be used to append one binary file to
          another (without creating a new file).
          

          
4. Data file formats
               The preferred and more commonly used format, as described below,
          consists of one or more records per file.  Each record consists of 100
          4-byte words of header information followed by spectral data.  Many
          items listed are not always present, depending on how the data
          file was generated.  The items with an asterisk (*) are the most
          important ones, and are used by the plotting software to
          distinguish between valid (plottable) and invalid files.
          
             Word   Description             Word   Description
               *1   Record number          ** 21   Noise flag (1=noise)
               *2   Channel number         ** 22   Std. dev. of phase
               *3   Mirror position           23   Beginning time (HHMMSS)
                      0 = earth               24   Current time (HHMMSS)
                      4 = hot blackbody      +25   Quality flag
                      8 = cold blackbody              1 = ifgm,ok
                4   Scan direction(1,2)               2 = spectrum,ok
                5   Mirror-alignment flag             <0 = rejected
                6   Buffer overflow flag     +26   Data conversion type
                7   No. unknown records             1:I*2, 2:I*4, 3:R*4
                8   No. points in ifgm.      +27   ZPD word number (in ifgm)
                9   Beginning record number   28   Time correction (seconds)
                    (raw data rec.no. for     29   Apodization indicator
                     start of ifgm.)                     (0=none)
               10   ZPD rec.no. (raw data)    30   No. ifgm. points used if FFT
               11   Time (seconds)           *31   No. points in spectrum
               12   Hot blackbody temp.(C)    32   Calibration record 1
               13   Cold blackbody temp.(C)  *33   Interval in indep.var.
               14   DC Level, Ch. 1          *34   Minimum value, indep.var.
               15   DC Level, Ch. 2          *35   Maximum value, indep.var.
               16   DC Level, Ch. 3          *36   Number of 32-bit words/record
               17   Year                      37   Number of header words (100)
               18   Month                     38   Spectral resolution
               19   Day                       40   Number of records in file
            ** 20   Flag for "bad"        41..46   Blackbody temps & calib.recs.
                    (short or small zpd)      51   Aircraft Latitude
                                              52   Aircraft Longitude
                                              53   Aircraft Altitude
                                              54   Aircraft Heading
          

          Additions and changes:
          
          Words 41 .. 46:
               41  Average HBB temp, cal.pt. 1
               42  Average CBB temp, cal.pt. 1
               43  Average HBB temp, cal.pt. 2
               44  Average CBB temp, cal.pt. 2
               45  Record number, in cal.file, of cal.pt.1
               46  Record number, in cal file, of cal.pt.2
          21 May 91 --In files written by HISAC1.EXE:
               61..78 Averages of the SCAM analog channels
          23 July 91 -- In files written by HISAC3.EXE:
               55..57 Temperature correction coefficients for the hot blackbody
               58..60 Temperature correction coefficients for the cold blackbody
          29 July 91 -- In files written by AVDIRS.EXE:
               81,82  Time (seconds) in "file1" and "file2", respectively
               83,84  Time (hhmmss) in "file1" and "file2", respectively
          2 August 91 -- In files written by COADDHIS.EXE:
               85   Mean spectral average
               86   Std. Dev. of spectral averages
               87   Lower limit (wavenumber) for spectral averaging
               88   Upper limit (wavenumber) for spectral averaging
               89   Aircraft heading at start of coadd period
               90   Aircraft heading at end of coadd period
          2 August 91 -- In files written by HISAC3.EXE:
               91   Average HBB temperature at first calibration point
               92   Std.dev. of HBB temp. at first calib. pt.
               93   Average CBB temperature at first calib. pt.
               94   Std.dev. of CBB temp. at first calib. pt.
           95..98   Same quantities as in 92..95, for second calib.pt.
          
          ** Important change!!
          25 September 91 -- in files written by HISAC1.EXE
               20   flag for "burst noise"
               21   flag for "bad" ifgm.
          25 September 91 -- in files written by HISAC2.EXE
               22   standard deviation of phase
          
          5 November 91 -- in files written by HISAC1.EXE
               39   flag for bad sequence of 3-bit record counter
          
          + NOTE: In the files of calibrated spectra, words 25, 26 and 27 are
            ambient temperature, hot blackbody emissivity and cold blackbody
            emissivity, respectively.