## Slide 1
Why is the Plume RGB Important?
The improved spatial, temporal and spectral attributes of the ABI allow for monitors plumes associated with rockets and other hotspots.
Instead of needing to show 3 or 4-panels with separate spectral bands, these RGBs combine information on the plumes from several key spectral bands: 3.9 micrometer or the “fire band”, the upper-level water vapor band (8), and the 7.3 micrometer (water vapor) band.
How is the Plume RGB Created?
Color | Band / Band (µm) | Range (Min –> Max) | Physically Relates to… | Gamma | Large Contribution to pixel indicates…
Red | 7 / 3.9 | 273 to 338 K | Plume temperature | 1.0 | Warm plume
Green | 8 / 6.2 | 220 to 280 K | Plume warming | 1.0 | Plume cloud
Blue (night) | 10 / 7.3 | 230 to 290 K | Plume warming | 1.0 | Plume cloud
  Application: This RGB can allow for a quick-look for signal associated with rocket plumes or other hot spots. The solar illumination determines if one wants to use the day or night version of this plume RGB. The IR-only “nighttime” version can be used both day and night.
  Primary Application Application: Viewing the spectral signatures associated with rocket launches.
Impact on Operations
  Limitations:
  - Care should be taken as the region of interest approaches the edge of the full disk.
  - The water vapor plume may be harder to detect, depending on the background.
  - The “blue” component can be overwhelmed by the 3.9 micrometer band.
  - May need to address limits for improved presentation.
  Thick clouds: Thick clouds or low-level moisture may hinder viewing the plume hotspot when it’s lower in the atmosphere.
Limitations
Plume RGB from GOES-16 ABI at 0029 UTC, 16 November 2020.
Warmer in water vapor bands
Contributor: Tim Schmit NOAA NESDIS STAR CORP ASPB http://cimss.ssec.wisc.edu/aspb/
Quick Guide (nighttime)
Rocket Plume RGB
Plume cloud

## Slide 2
RGB Interpretation
Resources
Source Name Title as a hyperlink
Source Name Title as a hyperlink
Source Name Title as a hyperlink
Size of this box can vary
Hyperlinks not available when viewing material in AIR Tool
Hot-spot (reddish)
1
1
Plume from GOES-16 ABI at 0701 UTC, 23 December 2021.
coastline
Comparison to other products: Similar to the Fire RGB with hotspots appearing red, similar to the airmass RGB, in that it leverages a mid-level water vapor band. The images shown on this page are of the GOES-S rocket launch from Cape Canaveral, Florida.
ABI 0.64 µm
Hot spot
Note:, colors may vary diurnally, seasonally, and latitudinally; plus with hotspots, plumes, moisture amount, etc.
RGB Color Guide
Quick Guide (nighttime)
Rocket Plume RGB
ABI 3.9 µm
Plume