Flight Summary NAST-Metop Flights

General Information

Flight date- 29 April 2007

Flight duration - 5.7 hours

Crew – Bill Rieke, John Bain

Instruments flown: NAST-I, NAST-M, SHIS, REVEAL (4)

Flight Log

| Engine Start | 9:30 | Takeoff | 9:40 | Approach | 3:05 |
| --- | --- | --- | --- | --- | --- |
| Data Rec On | 9:35 | Begin Descent | 2:43 | Landing | 3:16 |
| Gear extension/retractions |
| Gear Up | 9:40 | 3:00 |  |  |  |  |  |
| Gear Down | 2:43 | 3:11 |  |  |  |  |  |

Weather Observations
Cruise:

- The sky was clear with very slight haze obscuring the horizon.  Near the south end of the track small scattered “popcorn” cumulus clouds were near the ground in wide bands.  Near the northern end of the track some streaks of cirrus clouds were below and east of the track.

Flight Profile

We flew the profile as planned.  We climbed reaching 57K feet and flew north and south along a 170mile long line near that extended to about 250 miles south of New Orleans over the Gulf of Mexico..

Instrument Notes

- The NAST-M payload was out of operation for maintenance on its computer which had been removed.

- No fail indications for the flight for either NAST-I or SHIS.