Applications with New Multi-spectral Environmental Remote Sensing Satellites – Ostuni School

Menzel & Antonelli

Quiz 2

16 June 2006

Name:_________________________________________

1.	True – False

T   F   		Solar radiance is the same at the sun and earth surface.

T   F   		99% of the earth emitted irradiance comes from wavelengths greater than 4.0 μm.

T   F   	  	If blackbody A has a higher temperature than blackbody B, blackbody A will emit

more radiance at all wavelengths than blackbody B.

T   F   		If a planetary atmosphere is less absorbing in the visible wavelengths than at

infrared wavelengths, then the surface temperature of that planet is less than its

effective temperature.

T   F   	  	In the infrared window region on-H2O-line radiances are greater than off-H2O-line

radiances in cases of temperature inversions.

2.  	Multiple Choice

If the temperature of a 300 K blackbody increases by 1 % then:

the maximum Planck radiance (mW/m2/ster/μm) increases by

(a) 0% (b) 1%, (c) 2%, (d) 4%, or (e) 5%.

the irradiance (area under Planck curve) increases by

(a) 0%, (b) 1%, (c) 2%, (d) 4%, or (e) 5%.

the wavelength of the maximum Planck radiance (location of peak) decreases by

(a) 0%, (b) 1%, (c) 2%, (d) 4%, or (e) 5%.

3.	Associate the cloud test on the left with the appropriate description on the right.

[   ]	r1.38 > threshold				(a) finds low clouds over snow

[   ]	r.87 / r.66 between .9 and 1.1			(b) finds clouds over oceans

[   ]	BT3.9 - BT11 > 3 C				(c) finds high thin cirrus

[   ]	BT11 < 270 K					(d) indicates clouds in vegetated areas

[   ]	r1.6 > threshold				(e) tests for cloud edges

4.	A hot plume of industrial waste is obstructing the view of an infrared radiometer into the distance.  Thus the radiometer senses a hotter temperature.  What is the difference of the radiances sensed by the radiometer when viewing a clear sky FOV and then a plume contaminated FOV?  Use the indicated transmittances and blackbody radiances for background, plume, and foreground to calculate your answer.

background		plume		foreground

temperature			Tb = 300		Tp = 340	Tf = 300

(degrees Kelvin)

bb radiance			Bb = 115		Bp = 195	Bf = 115

(mW/m2/ster/cm-1)

transmittance			(b = 0.9		(p = 0.3	(f = 0.9

A(

B(

C(

D(

E(

5.  Identify the spectra with the scene

[   ]  somewhat moist clear sky over sea

[   ]  ice cloud

[   ]  very dry land (e.g. desert)

[   ]  opaque thick cloud

[   ]  dry clear sky over sea