## Slide 1: GOES-R Series Data Access
GOES-R Series Training
AMS Short Course
January 2019
Notes: Changes:
Added CIRA Central America site http://rammb.cira.colostate.edu/ramsdis/online/rmtc.asp

## Slide 2: Contributors
Jim McNitt 1, Matt Seybold 2, Kathryn Mozer 2, Seth Clevenstine1, Natalia Donoho1, Hongming Qi1, Richard Antoine1, Donna McNamara 3, Alan Hall 3, and Ed Kearns4
Office of Satellite and Product Operations (OSPO),
National Environmental Satellite, Data, and Information Service (NESDIS)
National Oceanic and Atmospheric Administration (NOAA)
Affiliations: 1 Satellite Products and Services Division; 2 GOES-R Product Readiness and Operations Team, 3 Mission Operations Division; 4 NOAA Big Data Project
Additional Acknowledgements: University of Wisconsin – Madison, SSEC/CIMSS

## Slide 3: Agenda
Objectives of Lesson
Overview of the Office of Satellite and Product Operations
Overview of GOES-R Series Data Access
GOES Rebroadcast (GRB)
High Rate Information Transmission/ Emergency Managers Weather Information Network (HRIT/EMWIN)
Production Distribution and Access (PDA)
Comprehensive Large Array-data Stewardship System (CLASS)
GOES Data Collection System (DCS)
GEONETCast Americas (GNC-A)
NOAA Big Data Project – Cloud Access
Internet Access - Websites

## Slide 4: Objectives of the Lesson
By the end of the lesson the participant should:
  Understand the GOES-R Series data sources and which products are available from each source
  Gain a basic understanding of the GOES Rebroadcast (GRB), High Rate Information Transmission/ Emergency Managers Weather Information Network (HRIT/EMWIN), and GEONETCast Americas (GNC-A)
  Understand what function the Production Distribution and Access (PDA) provides and its relationship to the other sources of GOES-R Series data products
  Understand how to retrieve data from the Comprehensive Large Array-data Stewardship System (CLASS)
The participants will be provided information on User Groups
The participants will be provided links to Websites, Unidata/UCAR, and the Big Data Project that can be used to retrieve products

## Slide 5: Satellite and Product Operations
NOAA NESDIS Office of Satellite and Product Operations
  Performs command and control of United States operational weather satellites
  Operates ground sites for command and control; and for data acquisition and retransmission
  Produces derived products from satellite observations and distributes those products to authorized users in near real-time or to the archive for use by the scientific community

## Slide 6: GOES Constellation
Preparing for GOES-West Ops
GOES-17
137.2° West
GOES-West
GOES-15
128° West
GOES-East
GOES-16
75.2° West
Standby
GOES-14
105° West
Storage
GOES-13
60° West
GOES-West
GOES-17
137.2° West
Supplemental Operations
GOES-15
128° West
GOES-East
GOES-16
75.2° West
Standby
GOES-14
105° West
Storage
GOES-13
60° West
GOES-West
GOES-17
137.2° West
Storage
GOES-15
128° West
GOES-East
GOES-16
75.2° West
Standby
GOES-14
105° West
Storage
GOES-13
60° West
Current as of
Dec 20, 2018
Plan for
January 2019
6 months
after GOES-17
assigned to
GOES-West

## Slide 7: Overview of GOES-R Series Data Access
Acronym | System Name | Description
GRB | GOES Rebroadcast | The primary relay of full resolution, calibrated, near-real-time broadcast of GOES-R for Level 1b data products (Advanced Baseline Imager L1b, Space Weather L1b, and Geostationary Lightning Mapper L2). These data are available to all users with GRB receivers in view of a GOES-R series satellite at the East or West operational longitudes.
HRIT/ EMWIN | High Rate Information Transmission/ Emergency Managers Weather Information Network | The HRIT/EMWIN service is a new high data rate (400 Kbps) broadcast for GOES-R satellite imagery and selected products to remotely-located user terminals. Combines LRIT and the EMWIN direct broadcast service that provides users with weather forecasts, warnings, graphics and other information directly from the NWS in near real-time. Also included is a copy of GOES-DCS.
PDA | Product Distribution and Access | The Environmental Satellite Processing and Distribution System is responsible for receiving and storing real-time environmental satellite data and products and making them available to authorized users. It is located in the Environmental Satellite Processing Center at the NOAA Satellite Operations Facility in Suitland, Maryland. The Product Distribution and Access (PDA) component of ESPDS provides real-time distribution and access services for GOES-R users through a terrestrial network.
CLASS | Comprehensive Large Array-data Stewardship System | Web-based data archive and distribution system for NOAA’s environmental data. CLASS will provide retrospective data access and distribution services of GOES-R data to all users.

## Slide 8: Overview of GOES-R Series Data Access
Acronym | System Name | Description
GNC-A | GEONETCast Americas | GEONETCast Americas is the Western Hemisphere component of GEONETCast, a near real time, global network of satellite-based data dissemination systems designed to distribute space-based, air-borne and in situ data, metadata and products to diverse communities.
Websites | Websites on the Internet | NOAA, NASA, NOAA Cooperative Institutes, and Universities distribute GOES-16 imagery on their websites. Many universities receive data from Unidata. Unidata has GRB and NOAPort receive stations
BDP | Big Data Project | Demonstration Project. The BDP, through Cooperative Research and Development Agreements (CRADAs), currently works with five infrastructure-as-a-service (IaaS) providers to broaden access to NOAA’s data resources.
NOAAPort | NWS Satellite Broadcast Network | GOES-R will provide selected products to the NWS Advanced Weather Interactive Processing System (AWIPS) Satellite Broadcast Network and NOAAPort. Sectorized Cloud and Moisture Imagery (SCMI) will be delivered via SBN/NOAAPort

## Slide 9: GOES-R Series GOES Rebroadcast
The GOES Rebroadcast (GRB) provides the primary relay of GOES-R Series full resolution, calibrated, near-real-time direct broadcast Level 1b data from the Advanced Baseline Imager and the Space Weather instruments and Level 2 data from the Geostationary Lightning Mapper
The GRB downlink is standards-based and documented in the Product Definition and Users’ Guide and Downlink Specifications
DVB-S2
CCSDS
Product Definition and
Users’ Guide
GRB
Downlink Specifications for
Users
Consultative Committee for Space Data Systems
Digital Video Broadcasting
Notes: The GOES Rebroadcast (GRB) provides the primary relay of full resolution, calibrated, near-real-time direct broadcast space relay of Level 1b data from each instrument and Level 2 data from the Geostationary Lightning Mapper (GLM)
The GRB downlink is standards-based, making use of the following protocols:
  Digital Video Broadcasting (DVB-S2)
  Consultative Committee for Space Data Systems (CCSDS) Advanced Orbiting Systems (AOS)
  Space Data Link Protocol
  CCSDS Space Packet Protocol

## Slide 10: GOES-16 Products on GRB
    Level 1b Products:
    Radiances from the Advanced Baseline Imager: 16 Bands; Full Disk, CONUS, and Mesoscale
    Solar imagery from the Solar Ultraviolet Imager
    Solar flux from the Extreme Ultraviolet and X-ray Irradiance Sensors
    Energetic heavy ions from the Space Environment In-Situ Suite
    Space environment magnetic field from the Magnetometer
Level 2 products:
  Geostationary Lightning Mapper
Space Weather Products
Notes: Level 1b products:
  Radiances from Advanced Baseline Imager: 16 Bands; Full Disk, CONUS, and Mesoscale
  Solar Imagery from Solar Ultraviolet Imager
  Solar Flux from the Extreme Ultraviolet and X-ray Irradiance Sensors
  Energetic Heavy Ions from the Space Environment In-Situ Suite
Level 2 products:
  Geostationary Lightning Mapper

## Slide 11: GRB Specifications
 | GOES Rebroadcast (GRB)
Full Disk Image | 5 mins (Mode 4), 15 mins (Mode 3), and 10 mins (Mode 6)
Other Modes | 3000 km X 5000 km (CONUS: 5 minute) 1000 km X 1000 km (Mesoscale: 30 seconds)
Polarization | Dual Circular Polarized
Receiver Center Frequency | 1686.6 MHz (L-Band)
Data Rate | 31 Mbps
Antenna Coverage | Earth Coverage to 50
Data Sources | ABI (16 bands), GLM, SEISS, EXIS, SUVI, MAG
Space Weather | ~2 Mbps
Lightning Data | 0.5 Mbps
Notes: GRB replaces the GOES VARiable (GVAR) service
GRB provides improved products. ABI provides three times more spectral information, four times the spatial resolution, and more than five times faster temporal coverage than the previous system

## Slide 12: GOES Rebroadcast Reception
Reception of the GOES Rebroadcast (GRB) data is accomplished by means of a fixed dish antenna with a dual left and right hand circular feed horn connected to two Low Noise Amplifiers
The Low Noise Amplifiers outputs are connected to Radio Frequency/ Intermediate Frequency down-converters
The Radio Frequency/ Intermediate Frequency down-converters are connected to Digital Video Broadcasting-S2 (DVB-S2) capable receivers
The GRB downlink signal from the satellite is at a center frequency of 1686.600 MHz and requires an Antenna gain-to-noise-temperature (G/T) of 15.2 dB/K for worst-case locations

## Slide 13: GRB Reception
Modulation is either
  8PSK with a symbol rate of 7.825768 Million symbols per second (Msps) with a rate 2/3 Forward Error Correction coding
  QPSK with a symbol rate of 8.665938 Million symbols per second (Msps) with a rate 9/10 Forward Error Correction coding*
Nominal antenna size: 4.5 meter dish with a system noise temperature of 120 K
A dual circular polarization is used to accommodate the 31 Mbps data rate
See the next slide for product allocation on Right Hand Circular Polarized (RHCP) and Left Hand Circular Polarized (LHCP)
Note: The default modulation mode for GOES-16 is QPSK
GOES-R Documents are available at: https://www.goes-r.gov/resources/docs.html
GOES Rebroadcast (GRB) Downlink Specifications for Users, August 6, 2012
https://www.goes-r.gov/users/docs/GRB_downlink.pdf
GOES Rebroadcast Reception

## Slide 14: GRB Data Flow
Consolidated Backup (CBU) Fairmont, WV
Wallops Command and
Data Acquisition Station (WCDAS)
Wallops, VA
NOAA Satellite Operations Facility (NSOF)
Suitland, MD
GOES-East
75.2° West
GOES-17
137.2° West
Direct Broadcast Community
GRB
GRB and HRIT/EMWIN
Command & Control, Mission Data, GRB, and HRIT/EMWIN
GOES Storage
105° West
Instrument and Telemtry Data
Instrument and Telemtry Data
PDA
AWIPS
NCFs
SBN/NOAAPort
L1B and L2+ Derived Products
Climate Research and Academia
L1B, L2+
NOAA Port Community
SARSAT
DCS, HRIT/EMWIN
Command & Control, Mission Data, GRB
Sectorized Cloud and
Moisture Imagery
Authorized Operational Users
SARSAT
DCS
DCS
GRB

## Slide 15: GOES-R Series GRB Ground Antenna Sizes
NOTES:
Calculations based on available data as of May 2011.
Each antenna size is usable within the indicated contour.
Rain attenuations included are: 1.3/1.6/2.0/2.2/2.5 dB (3.8 to 6 m)
4. An operating margin of 2.5 dB was included in the calculations, but users are warned that may not be enough in parts of North America where cellular and mobile internet service providers may provide strong interference and therefore additional antenna gain may be needed.
GOES West
GOES East

## Slide 16
Community Satellite Processing Package for Geostationary (CSPP Geo)
ABI quicklooks (GRB package)
SUVI Imagery (GRB Package)
Himawari-8 AHI Imagery and Cloud products (GEOCAT package)
Himawari AHI Composite RGBs
ABI true color
Funded by NOAA GOES-R Program to create and distribute software to process direct broadcast data from geostationary satellites, generating products in real-time
All software is free to download and use
GOES-16 product software is available to:
  Process the GRB data stream, reconstructing the products that were generated on the ground system
  Further process ABI data to generate Level 2 products
In addition, software is available to process direct broadcast data from GOES-13, GOES-15 and Himawari-8.

## Slide 17: CSPP Geo Level 2 Processing
ABI Level 2 products are generated by research implementations of the operational algorithms, running in the “AIT Framework” which was developed at NOAA
Level 2 products were initially made available in CSPP Geo AIT Framework Beta, and are now in Version 1 (December 2018):
  Aerosol Detection: Smoke and Dust
  Cloud Top Height
  Aerosol Optical Depth
  Cloud Top Phase
  Clear Sky Mask
  Cloud Top Pressure
  Cloud and Moisture Imagery
  Cloud Top Temperature
  Cloud Optical Depth (day/night)
  Land Surface Temperature (skin)
  Cloud Particle Size Distribution (day/night)
GOES-16 Land Surface Temp.
GOES-16 Cloud Top Height

## Slide 18: GRB User Readiness
Chart: 
| GOVERNMENT | COMMERCIAL | ACADEMIC | MILITARY | INTERNATIONAL | SKYWARN
 | 32 | 14 | 7 | 10 | 19 | 1
100 GRB receive stations are accounted for (planned and installed)
83 GRB receive stations are installed
56 are receiving GOES-16 GRB (including spares)
21 are receiving GOES-17 GRB
2 plan to receive GOES-17 when it is declared GOES West
18
32
Government
19
International
14
Commercial
10
Military
7
Academic
1 SKYWARN
GRB Receive Station = 1 antenna and 1 receiver

## Slide 19: GRB Site Status
Updated on March 13, 2018

## Slide 20: HRIT/EMWIN
The High Rate Information Transmission (HRIT) / Emergency Managers Weather Information Service (EMWIN) broadcast is operational on GOES-16 with a data relay capacity of 400Kbps
However, the EMWIN content on HRIT/EMWIN, virtual channels 20 – 22, is in test mode and is expected to be operational in May 2019
The initial HRIT/EMWIN product offering includes:
  EMWIN products includes National Weather Service watches, warnings, forecasts and graphics
  Copy of the GOES-DCS observations
  Environmental maritime products from National Hurricane Center
  Additional 4 km resolution GOES-15 & Himawari-8 IR/WV/Visual Imagery (GOES-17 only)
  GOES-16 & 17 Imagery – ABI Cloud and Moisture Imagery (CMI) converted to the 2013 CGMS Global LRIT/HRIT standard
    2 kilometer spatial resolution ABI Full Disk Bands 2, 7, 8, 9, 13, 14 and 15 available every 30 minutes
    ABI mesoscale imagery in Bands 2, 7 and 13 available every 15 minutes (Band 2 is .5 km while Bands 7 and 13 are 2 km resolution)

## Slide 21: HRIT/EMWIN
EMWIN
EMWIN products will be transmitted as a contiguous file on the HRIT/EMWIN broadcast, a departure from the Quick Block Transfer (QBT) protocol packet transmission from GOES NOP series broadcasts
Retransmissions of EMWIN Priority 1 products are enabled 5 seconds apart if an data dissemination outage or noisy radio frequency environments are observed
File Names. The EMWIN file naming convention has been revised to follow the WMO format identified in WMO Pub 386.
  More information can be found at http://www.nws.noaa.gov/emwin/index.htm
Quarterly HRIT/EMWIN User Group Meetings
The latest HRIT/EMWIN Stakeholder/User Group meeting was held on December 6th, 2018, next user group meeting is planned for sometime in March 2019 (held quarterly)
  Contact seth.clevenstine@noaa.gov to participate in HRIT/EMWIN User Group meetings and added to the email distribution list for HRIT outages/notifications

## Slide 22: HRIT/EMWIN Processing Chain
NSOF Product Distribution and Access (PDA)
G16
G17
Consolidated Backup
FEP-2
FEP-1
FEP-0
CBU Product Distribution and Access (PDA)
Wallops Acquisition Station
G16 Primary
G17 Backup
G16 Backup
G17 Primary
G16 Backup
G17 Backup
CBU HRIT Broadcast Subscriptions
GOES-16/17 CMI
(NSOF/CBU)
DADDS DCS Data (NSOF/WCDAS)
NSOF HRIT Broadcast Subscriptions
EWMIN (College Park/Boulder)
Internet Data (NHC & NWS)
Legacy GOES
(NSOF/CBU)
NSOF HRIT Broadcast Stream Services
CBU HRIT Broadcast Stream Services
FEP-4
FEP-3
FEP-2
FEP-1
FEP-0
GOES-17
137.2° West
GOES-16
75.2° West

## Slide 23: HRIT/EMWIN Users By Numbers
Chart: HRIT/EMWIN Users by the Numbers
| Government | Department of Defense | Amateur | Academic | Vendor/Manufacturer | Commercial | International
 | 41 | 34 | 21 | 3 | 11 | 4 | 7
Chart: HRIT/LRIT Site Status
| HRIT Ready | Planned HRIT Sites | LRIT Sites, No Plans for HRIT
 | 121 | 33 | 25
Users are defined as a having a complete receiving station capable of obtaining the HRIT/EMWIN broadcast downlink

## Slide 24: HRIT/EMWIN Reception
To receive HRIT/EMWIN, a user can purchase the necessary equipment (antenna, cabling, receiver, computer, and software) from commercial companies for unlimited access to the GOES-R Series HRIT/EMWIN. A manufacturer’s list is available at: http://www.noaasis.noaa.gov/NOAASIS/ml/manulst.html
  Previous compatible 1.0+ meter LRIT antennas, cabling and majority of LNB downconverters can be reused for HRIT/EMWIN
  All LRIT 1691.0 MHz receivers will not work without modification or new 1694.1 MHz HRIT/EMWIN compatible receivers will need to be obtained
The transmission format; “The Coordination Group for Meteorological Satellites LRIT/HRIT Global Specification” can be downloaded from: https://www.cgms-info.org/documents/cgms-lrit-hrit-global-specification-(v2-8-of-30-oct-2013).pdf
The GOES-R Web Site provides program and technical information at: https://www.goes-r.gov/users/hrit.html
A software-based solution is described at the HRIT/EMWIN prototype receiver links and specifications webpage: https://www.goes-r.gov/users/hrit-links.html
There is no fee or license requirement required by NOAA to receive the products on HRIT/EMWIN
For any HRIT/EMWIN broadcast inquiries, please send an email to seth.clevenstine@noaa.gov for further information.

## Slide 25: GRB Reception
HRIT/EMWIN Reception Details
Component | HRIT/EMWIN Broadcast Specifications | Additional Information
Platform | Operational East and West GOES-R Series Satellites | GOES-16 at 75.2° West GOES-17 at 137.2° West
Broadcast | Operating Downlink Frequency Range | L-band
 | Center Frequency | 1694.1 MHz
 | Data Rate | 400 Kbps
 | Symbol Rate | 927,000 symbols per second (sps)
 | Modulation - BPSK | Convolutional rate ½ code with constraint length 7 concatenated with Reed Solomon (255,223) with Interleave = 4 Square Root Raised Cosine filtering using an Alpha factor of 0.3 The resulting “Necessary Bandwidth” for this signal will be 1.205 MHz
 | Polarization - Linear | Vertical Offset
Antenna System | VSAT | At 5 degree elevation, the minimum antenna is 1.2 meter. At 10 degrees or more elevation the minimum size is 1.0 meter
Low-Noise Block-Down Converter | L-band | Example: Input 1691 MHz Output 137.5 Mhz
Satellite Receiver | L-band | BPSK 1691 MHz to 137.5 MHz
Software | N/A | De-encapsulates HRIT/LRIT files Visualization and Manipulation of Files Optional Applications (examples) EMWIN visualization application GOES-DCS database software or application

## Slide 26: GOES Data Collection System
The GOES DCS is a relay system used to collect information from a large number of Earth-based platforms that transmit in-situ environment sensor data on predefined frequencies and schedules
In the GOES-R era, the number of user-platform channels has expanded from 266 to 433. There is also a frequency change from 1695 MHz to 1679 MHz, for the Direct Readout Ground Stations (DRGS)
Data transmission rates are 300 bps and 1200 bps
There are approximately 30,000 active DCPS (of 40,000 deployed)
Most transmit every hour. There are some platforms that transmit data every half hour and a number of platforms that transmit every 15 minutes
Tide Gages monitoring for tsunamis report every 5 or 6 minutes.
DCS relays 800,000 messages per day
An estimated 8,000,000 (million) observations per day are distributed through the global observing system
There 800 user agencies/organizations
There are 1,200 individual users registered for system access

## Slide 27: Baseline Products
ADVANCED BASELINE IMAGER (ABI)
    Aerosol Detection (Including Smoke and Dust)
            Aerosol Optical Depth (AOD)
            Clear Sky Masks
            Cloud and Moisture Imagery*
            Cloud Optical Depth
            Cloud Particle Size Distribution
            Cloud Top Height
            Cloud Top Phase
            Cloud Top Pressure
            Cloud Top Temperature
            Derived Motion Winds
            Derived Stability Indices
            Downward Shortwave Radiation: Surface
Fire/Hot Spot Characterization
Hurricane Intensity Estimation
Land Surface Temperature (Skin)
Legacy Vertical Moisture Profile
Legacy Vertical Temperature Profile
Radiances
Rainfall Rate / QPE
Reflected Shortwave Radiation: TOA
Sea Surface Temperature (Skin)
Snow Cover
Total Precipitable Water
Volcanic Ash: Detection and Height
Note: *Key Performance Parameter (KPP)
Notes: GOES-R SERIES PRODUCT DEFINITION AND
USERS’ GUIDE
(PUG)
VOLUME 1: MAIN
VOLUME 2: L0 PRODUCTS
VOLUME 3: LEVEL 1B PRODUCTS
VOLUME 4: GOES-R REBROADCAST (GRB)
VOLUME 5: LEVEL 2+ PRODUCTS
APPENDIX X: ISO SERIES METADATA

## Slide 28: Baseline Products
GEOSTATIONARY LIGHTNING MAPPER (GLM)
Lightning Detection: Events, Groups & Flashes
SPACE ENVIRONMENT IN-SITU SUITE (SEISS)
Energetic Heavy Ions
Magnetospheric Electrons & Protons: Low Energy
Magnetospheric Electrons & Protons: Med & High Energy
Solar & Galactic Protons
MAGNETOMETER (MAG)
Geomagnetic Field
EXTREME ULTRAVIOLET AND X-RAY IRRADIANCE SENSORS (EXIS)
Solar Flux: EUV
Solar Flux: X-ray Irradiance
SOLAR ULTRAVIOLET IMAGER (SUVI)
Solar EUV Imagery

## Slide 29
Environmental Satellite Processing and Distribution System
The Environmental Satellite Processing and Distribution System (ESPDS) is an enterprise system for ingesting, producing delivering near real-time data to our core, time critical users. It is located in the Environmental Satellite Processing Center (ESPC) and includes the following major segments:
  Product Generation - NOAA Data Exploitation (NDE)
  Product Distribution – Production Distribution and Access (PDA)
  Re-broadcast HRIT/EMWIN and GNC-A
  High-speed network and services – Enterprise Infrastructure (EI)
PDA capabilities:
  Peers with high speed wide area network (N-WAVE)
  Greater security (secure transfer protocols, baseline monitoring, high performance threat scanning, etc.)
  Configurable production with custom tailoring capability

## Slide 30: GOES Data Operations in the ESPC
GOES-16/17
GRB
AWIPS
GOES-16/17
PPZ
Users
PDA
GOES-14/15
GEOPROD
Misc PG (SFS)
GEODIST
Users
Wallops CDA
Wallops Critical Infrastructure Protection (Backup)
GOES-14/15
GEOPROD
CIP
Misc PG
GEODIST
CIP
Users
GOES-16/17
GRB
Hot Backup
Cold Backup
Nominal Operations
Flow activated during Backup
Legend
Backup Operations
Consolidated Backup
(CBU)
Environmental Satellite Processing Center (ESPC)

## Slide 31: Production Distribution and Access
PDA service is dedicated for authorized near real-time users. Other near real-time distribution services are being explored as PDA is a finite resource
The PUSH services are available only to users with a 24x7 support desk
New user onboarding is currently suspended while the organization assesses time critical user needs and evaluates available capacity on the system
Data access information is available at:
http://www.ospo.noaa.gov/Organization/About/access.html
Must be signed by the Government official responsible for the data flow on the subscriber’s end
For existing users who contact ESPC about a problem:
  Make sure to say that you are a PDA user and provide our PDA user group name
  Provide PDA product names or exact files names for the data you are missing. The filename of the last data you received is most useful to help us pinpoint your problem quickly

## Slide 32: Comprehensive Large Array-data Stewardship System
CLASS is NOAA's Archive and delayed-mode distribution system for distribution of NOAA and US Department of Defense (DoD) Polar-orbiting Operational Environmental Satellite (POES) data, NOAA's Geostationary Operational Environmental Satellite (GOES) data, and derived data.
CLASS stores an average of 130 TB/month of data. The total amount of data at CLASS is almost 11 PB
A number of GOES-16/17 ABI Level 2 products are now available to the public through CLASS (GOES-17 data products have been available since November 28, 2018)
All available ABI products , as well as the L1B radiance data, are found under the GRABIPRD data family. For complete details on data maturity start dates and access dates please go to: https://www.ncdc.noaa.gov/data-access/satellite-data/goes-r-series-satellites
The GLM Level-2 products can now be ordered from CLASS under the Family name GOES-R Series GLM L2+ Data Product (GRGLMPROD)
Users need to be aware of any data caveats (warning) documented during the PS-PVR by clicking on the appropriate readme links provided
Note that CLASS is not a near real-time system and data availability is not guaranteed

## Slide 33: Levels of Access Services
CLASS order types: | Average completion time | Average File Limit | Contact the CLASS Help Desk?
Ad hoc orders (Use Search button to obtain inventory) | Usually within 12 to 24 hours | Up to 500 files | No
Large orders (use Quick Search button to skip inventory ) | 24 to 48 hours | 1000 to 3000 | No
Block orders (use Quick Search button) | > 48 hours | 3000 to 6000 | Yes
Subscription (standing orders) | < 6-7 hours | No limit | Yes

## Slide 34: Data Availability Times
The data availability in CLASS for S-NPP and JPSS-1 (NOAA-20) is about 4 hours. IDPS has a built in delay in order to ensure repaired granules make it to CLASS. CLASS changed the SNPP availability from 6 hours to 4 during 2018
GOES-N GOES-R POES JASON S-NPP JPSS
3 to 4 hrs
3 to 4 hrs
4 to 5 hrs
4 hrs
3 to 4 hrs
Notes: CLASS changed the S-NPP from 6 hours to 4 this year. After working JPSS, CLASS was able to reduce the time to get the repaired granuals quicker.

## Slide 35: GOES-16/17 Data Products from CLASS
How to request GOES-16 data products from CLASS
Start at the following link:
https://www.class.ncdc.noaa.gov/saa/products/welcome
  Then register
  Set up your user preferences
  Select data family to search
  Search for data
  Select files
  Review shopping cart
  Review your order status
A demonstration is available at:
https://www.class.noaa.gov/notification/demo.htm

## Slide 36: GEONETCast Americas (GNC-A)
GNC-A is the Western Hemisphere component of GEONETCast, a near real time, global network of satellite-based data dissemination systems designed to distribute space-based, air-borne and in situ data, metadata and products to diverse communities
12 Megabits per second data rate with Multiplexed C-Band DVB-S
Intelsat-21 Geostationary satellite at 58 degrees West
Footprint covers most of the Americas and Caribbean
GNC-A is providing GOES-16 Full Disk Cloud Moisture Imagery (CMI) Bands 2, 7, 8, 9, 13, 14, 15 (band 2 at 1 km and others at 2 km) every 15 minutes and Level-2 baseline products
GOES-17 Full Disk CMI on the above 7 bands and Level-2 baseline products will be provided once they reach the provisional maturity level
Selected JPSS imagery and products are available on GNC-A
Currently 81 GNC-A user stations from 19 countries in the Americas and Caribbean
More details about GNC-A on the presentation in Session 9B “National and International Education, Training, and user Readiness Activities for the New Generation Operational Environmental Satellite Systems”
Email for the point of contact for GNC-A: gnc.americas@noaa.gov

## Slide 37: GNC-A Broadcast
GEONETCast Americas Broadcast Parameter | Parameter Value
Satellite | IS-21 (Intelsat)
Location | 58 ° West or 302° East
PID | 4201
Transponder | 7C
Radio Frequency Band | C-band
Frequency | 3840 MHz
Frequency Range | 3700 – 4200 MHz
Symbol Rate: | 27.69 Msym
Polarization | Linear – Vertical (Horizontal or Vertical)
Typical Edge of Coverage e.i.r.p. (Effective Isotropic Radiated Power) | > 31.3 dBW
Datacasting Client Software (Required) | Kencast FAZZT Professional Client
FEC (Forward Error Correction – Kencast FAZZT) | 7/8
Peak G/T (antenna gain-to-noise-temperature) | Up to 2.5 dB/K

## Slide 38: GNC-A Community Map

## Slide 39: Data Access Options
5MBps 10 MBps 15 MBps 20 MBps 25 MBps 30 MBps
Bandwidth
14 Minutes
10 Minutes
8 Minutes
4 Minutes
2 Minutes
6 Minutes
12 Minutes
Data Latency
(From L1b generation to receipt by receive station)
GRB
GNC-A
HRIT/
EMWIN

## Slide 40: Big Data Project
NOAA’s Big Data Project (BDP) is designed to facilitate public use of key environmental datasets by providing copies of NOAA’s information in the Cloud, allowing users to do analyses of data and extract information without having to transfer and store these massive datasets themselves
http://www.noaa.gov/big-data-project
CICS-NC is a partner in the BDP and acts as a broker between NOAA and the public cloud providers
Links to Public Cloud Information and Datasets
  GOES-16/17 Data:
    Amazon Web Services
    Google Cloud Platform
    Open Commons Consortium
Notes: BDP Homepage:
http://www.noaa.gov/big-data-project
CICS-NC is a partner in the BDP and acts as a broker between NOAA and the public cloud providers
https://ncics.org/data/noaa-big-data-project/
Links to Public Cloud Information and Datasets
GOES-16 Data:
Amazon Web Services
Open%20Commons%20Consortium
IBM NOAA Data Portal
https://noaa-crada.mybluemix.net/node/33
Google Cloud Platform
https://console.cloud.google.com/launcher/details/noaa-public/goes-16?pli=1
Open Commons Consortium
http://edc.occ-data.org/goes16/getdata/

## Slide 41: Unidata/UCAR
Unidata/UCAR is currently making all GOES-16 and GOES-17 data available
Receiving GOES-16 GRB and GOES-17 GRB
Receiving GOES-16 products on NOAAPort
Methods of distribution include:
  McIDAS Abstract Data Distribution Environment (ADDE). ADDE is a Client/server data access model developed for McIDAS. Provides access for McIDAS-X, McIDAS-V, IDV, etc.) for NOAAPort and GRB-delivered content
  THREDDS Data Server (TDS) provides access for a variety of applications for NOAAPort and GRB-delivered content thredds-test.unidata.ucar.edu
  Website for NOAAPort and GRB delivered content
  Internet Data Distribution (IDD) is a real-time data "push" technology for NOAAPort and GRB-delivered content
    Projects -> Internet Data Distribution
    https://www.unidata.ucar.edu/projects/index.html#idd

## Slide 42: Websites
https://www.ncdc.noaa.gov/data-access/satellite-data/goes-r-series-satellites
https://www.star.nesdis.noaa.gov/GOES/

## Slide 43: Links to Websites
NOAA STAR GOES-16 Image Viewer
NOAA/NESDIS Geostationary Satellite Server
SSEC Geo Browser Color hybrid with GOES-16/17 and Suomi NPP
SSEC Geo Browser All bands, Meso1 Meso2 and CONUS and Full Disk, plus a "spectral" (all channels) loop geo imagery (SSEC Real Earth TM) All bands, CONUS and Full Disk and both meso-scale sectors
UW – Madison SSEC/CIMSS List of GOES-16 Websites
UW-Madison AOS Many sectors (including Southern Wisconsin) and several enhancements
RAMMB Slider GeoColor, all bands and all sectors
CIRA Central and South America and the Caribbean
ABI GOES-16/17 imagery (SPORT) 16 bands, RGBs, Full Disk and CONUS and Meso-scale sectors weather.us US view, several options
Meteo-Chile 16 bands and RGB images over Chile and 1-page band fact sheets
Brazil's CPTEC All ABI bands in animation over South America.
UNAM
Fuerza Aérea Colombiana
Notes: NOAA STAR GOES-16 Image Viewer https://www.star.nesdis.noaa.gov/GOES/GOES16_CONUS.php
NOAA/NESDIS Geostationary Satellite Server http://www.goes.noaa.gov/index.html
SSEC Geo Browser Color hybrid with GOES-16 and Suomi NPP http://www.ssec.wisc.edu/data/geo/#/animation?satellite=goes-16&end_datetime=latest&n_images=4&coverage=conus&channel=rgbstr&image_quality=gif&anim_method=javascript
SSEC Geo Browser All bands, Meso1 Meso2 and CONUS and Full Disk, plus a "spectral" (all channels) loop geo imagery (SSEC Real Earth TM) All bands, CONUS and Full Disk and both meso-scale sectors
https://www.ssec.wisc.edu/data/geo/#/animation?satellite=goes-16
UW-Madison AOS Many sectors (including Southern Wisconsin) and several enhancements
http://www.aos.wisc.edu/weather/wx_obs/GOES16.html
RAMMB Slider GeoColor, all bands and all sectors http://rammb-slider.cira.colostate.edu/
ABI GOES-16 imagery (SPORT) 16 bands, RGBs, Full Disk and CONUS and Meso-scale sectors weather.us US view, several options
https://weather.msfc.nasa.gov/sport/
Meteo-Chile 16 bands and RGB images over Chile and 1-page band fact sheets
http://www.meteochile.cl/PortalDMC-web/index.xhtml
Brazil's CPTEC All ABI bands in animation over South America.
http://pyata.cptec.inpe.br/acervowebv2/loop.show.logic
UNAM http://www.lanot.unam.mx/
Fuerza Aérea Colombiana https://www.simfac.mil.co/news.php

## Slide 44: Links to Websites
Embry Riddle Aeronautical University (Daytona Beach, FL campus)
GLM NASA SPoRT
GLM Univ of Maryland
Notes: Embry Riddle Aeronautical University (Daytona Beach, FL campus)
http://wx.erau.edu/erau_sat/
GLM NASA SPoRT
https://weather.msfc.nasa.gov/cgi-bin/sportPublishData.pl?dataset=goeseastglm&product=group&loc=conus
GLM Univ of Maryland
hhttp://lightning.umd.edu/Apps/GoesCesium/

## Slide 45: Other Data Access Links
NOAA satellite direct broadcast systems (GRB, HRIT, EMWIN, HRD, GNC-A)
http://www.noaasis.noaa.gov/NOAASIS/ml/satservices.html
NOAA Centers for Environmental Information (NCEI) portal NOAA/NESDIS CLASS
http://www.class.ngdc.noaa.gov/saa/products/welcome
Cloud services (experimental)
  AWS: https://aws.amazon.com/public-datasets/goes/
  Google: https://console.cloud.google.com/launcher/details/noaa-public/goes-16?pli=1
  OCC: http://edc.occ-data.org/goes16/getdata/
NESDIS websites:
    NOAA/NESDIS Geostationary Satellite Server http://www.goes.noaa.gov/index.html
    NOAA/NESDIS GOES-East Image Viewer https://www.star.nesdis.noaa.gov/GOES/index.php

## Slide 46: Notifications, Status, and Contacts
24/7 Help Desk | ESPCOperations@noaa.gov
ESPC Messages | https://www.ospo.noaa.gov/Operations/messages.html
User Services | SPSD.UserServices@noaa.gov
Data Access | NESDIS.Data.Access@noaa.gov
Facebook | https://www.facebook.com/NOAASatellites/
Twitter | https://twitter.com/NOAASatellites
GOES Status | https://www.ospo.noaa.gov/Operations/GOES/status.html
GOES User Information and Documents | https://www.ospo.noaa.gov/Operations/GOES/documents.html
Direct Services | https://noaasis.noaa.gov/NOAASIS/
GRB User Group | James.mcnitt@noaa.gov
Notes: 24/7 Help Desk
ESPCOperations@noaa.gov
ESPC Messages
http://www.ssd.noaa.gov/PS/SATS/messages.html
User Services
SPSD.UserServices@noaa.gov
Data Access
NESDIS.Data.Access@noaa.gov
Facebook
www.facebook.com/NOAANESDIS
Twitter
www.twitter.com/noaasatellites
Press releases
http://www.nesdis.noaa.gov/news_archives/
GOES Status
http://www.ospo.noaa.gov/Operations/GOES/status.html
GOES User Information and Documents
http://www.ospo.noaa.gov/Operations/GOES/documents.html
Direct Services
http://noaasis.noaa.gov/NOAASIS/
Other Links:
NOAASIS Website
http://noaasis.noaa.gov/NOAASIS/
List of GRB Vendors and Manufacturers at:
http://www.noaasis.noaa.gov/NOAASIS/ml/manulst.html
GOES-R Website
https://www.goes-r.gov/
GOES-R Product Definition and Users' Guide (PUG) Volume 4 http://www.goes-r.gov/users/docs/PUG-GRB-vol4.pdf
GRB Downlink Specification
http://www.goes-r.gov/users/docs/GRB_downlink.pdf

## Slide 47: Summary
There are a number of alternatives for obtaining GOES-R Series data products:
  GOES Rebroadcast (GRB) is the fastest and most reliable way. It is also the most expensive for the user
  High Rate Information Transmission/ Emergency Managers Weather Information Network (HRIT/EMWIN) provides low-resolution imagery. Cost to user is less than GRB. There is a delay due to processing at ESPC
  GEONETCast Americas (GNC-A) provides a subset of products. Cost to user is less than GRB. There is a delay due to processing at ESPC and distribution to NOAA’s contractor
  Production Distribution and Access (PDA). PDA service is dedicated for authorized near real-time users. New user onboarding is currently suspended while the organization assesses time critical user needs and evaluates available capacity on the system
  Comprehensive Large Array-data Stewardship System (CLASS). Level 1b and Level 2 products available with a delay
  Internet Access
Point of Contact: Jim McNitt, Email: james.mcnitt@noaa.gov

## Slide 48: Acronyms
ABI | Advanced Baseline Imager
AIT | Algorithm Integration Team
AOS | Advanced Orbiting Systems
AWIPS | Advanced Weather Interactive Processing System
BDP | Big Data Project
CBU | Consolidated Backup
CCSDS | Consultative Committee for Space Data Systems
CMI | Cloud Moisture Imagery
DADDS | DCS Administration and Data Distribution System
CFDP | CCSDS File Delivery Protocol
CICS-NC | NOAA Cooperative Institute for Climate and Satellites – North Carolina
CIMSS | Cooperative Institute for Meteorological Satellite Studies

## Slide 49: Acronyms
CIP | Critical Infrastructure Protection
CLASS | Comprehensive Large Array-data Stewardship System
DRO | Direct Readout
DVB-S2 | Digital Video Broadcasting
DCS | Data Collection System
DoD | Department of Defense
EIRP | Equivalent Isotropically Radiated Power
EOC | Edge of Coverage
ESPC | Environmental Satellite Processing Center
ESPDS | Environmental Satellite Processing and Distribution System

## Slide 50: Acronyms
EXIS | Extreme Ultraviolet and X-ray Irradiance Sensors
FEC | Forward Error Correction
FEP | Front End Processor
GLM | Geostationary Lightning Mapper
GNC-A | GEONETCast Americas
GOES | Geostationary Operational Environmental Satellites
GRB | GOES Rebroadcast
GVAR | GOES Variable
G/T | Antenna gain-to-noise-temperature
GTS | Global Telecommunication System (GTS)
HRR | Handover Readiness Review
JPSS | Joint Polar Satellite System
KPP | Key Performance Parameter

## Slide 51: Acronyms
HRIT/EMWIN | High Rate Information Transmission/ Emergency Managers Weather Information Network
LNA | Low Noise Amplifier
LZSS | Level Zero Storage System
NESDIS | National Environmental Satellite, Data, and Information Service
NHC | National Hurricane Center
NOAA | National Oceanic and Atmospheric Administration
NSOF | NOAA Satellite Operations Facility
NWS | National weather Service
OSPO | Office of Satellite and Product Operations
PDA | Production Distribution and Access
PLT | Post Launch Test
PUG | Product Definition and Users’ Guide
PS-PVR | Peer Stakeholder – Product Validation. Reviews

## Slide 52: Acronyms
NDE | NPP Data Exploitation
PLPT | Post Launch Product Testing
QC | Quality Control
SCMI | Sectorized Cloud and Moisture Imagery
SEISS | Space Environment In-Situ Suite
S-NPP | Suomi National Polar-orbiting Partnership
SSEC | Space Science and Engineering Center
SUVI | Solar Ultraviolet Imager i
WCDAS | Wallops Command and Data Acquisition Station
XPI | Cross-Polarization Interference