## Slide 1
ABI on The GOES-R Series
Tim Schmit Madison, WI
American Meteorological Society 99th Annual Meeting Phoenix, AZ • January 5-10, 2019
Thanks to Mat Gunshor, CIMSS and many others

## Slide 2
GOES-R Advanced Baseline Imager (ABI)
  Spectral
    Improved!
  Spatial
    Improved!
  Temporal
    Improved!
  Calibration
    Improved!
Lockheed Martin

## Slide 3: Question
How many total images (for a given band) per hour from one ABI in “flex” mode (or mode 3)?
a) 4
b) 12
c) 120
d) 136
e) 138

## Slide 4
Meso-scale box locations are movable
15 min (or 10 min in mode 6)
5 min
1 min
1 min
Scan mode (3) or ‘flex mode’ for the ABI:
Full disk every 15 min
+ 5 min CONUS
+ 1-min mesoscale (2 locations).
Mat Gunshor, CIMSS
Notes: 1-km2 spatial resolution at satellite nadir. Pixel Areas are approximate. Each bin is rounded to the nearest 1km2 until we get to 9.5km2 and then all are binned into the red 10+ area. So the first, dark blue, ring covers pixel areas from 1 to 1.49km2 and is labeled “1”, above 1.5 to below 2.5km2 goes into the next ring and is called “2”, etc. GOES-West location. Proposed CONUS sector, approved by the NWS NOAT. Two meso-scale image sectors shown; these are selectable. The same central lat/lon used for these mesoscales produces a different sized and shaped area for different satellite locations.

## Slide 5
15 min or 10 min in mode 6
Meso-scale box locations are movable
5 min
1 min
1 min
Scan mode (3) or ‘flex mode’ for the ABI:
Full disk every 15 min
+ 5 min CONUS
+ 1-min mesoscale (2 locations).
Mat Gunshor, CIMSS
Notes: 1-km2 spatial resolution at satellite nadir. Pixel Areas are approximate. Each bin is rounded to the nearest 1km2 until we get to 9.5km2 and then all are binned into the red 10+ area. So the first, dark blue, ring covers pixel areas from 1 to 1.49km2 and is labeled “1”, above 1.5 to below 2.5km2 goes into the next ring and is called “2”, etc. GOES-East location. Proposed CONUS sector, approved by the NWS NOAT. Two meso-scale image sectors shown; these are selectable. The same central lat/lon used for these mesoscales produces a different sized and shaped area for different satellite locations.

## Slide 6: Scan Mode 3 Timeline (Flex Mode) Delivers Storm Watch Every 30 Seconds
Meso: one every 30 seconds or two at 1 minute intervals each
Scene locations can be changed on the fly (no interruption of timeline)
30 seconds
MISTiC
Full
Disk
Meso
(north
swath)
CONUS
Nadir
Vis Star
Spacelook
Blackbody
IR Star
Note: Autonomous spacelook collected with each Full Disk swath
Meso
(south
swath)

## Slide 7: ABI - 5 times faster coverage
GOES-16: Previous:
Flex Mode Routine
Full Disk: 15 min 3-hr
CONUS: 5 min 15-min
Mesoscale: 1-min n/a
or 30-sec
PLUS – Flex mode scanning!
Credit: Rick Kohrs and Margaret Mooney, CIMSS

## Slide 8
Default Meso Locations
Two meso from GOES-West and two from GOES-East
Mat Gunshor, CIMSS

## Slide 9
ABI Band | Wavelength (µm) | Wavelength range (µm) | Sub-point pixel spacing (km) | Descriptive Name
1 | 0.47 | 0.45 - 0.49 | 1 | “Blue”
2 | 0.64 | 0.60 - 0.68 | 0.5 | “Red”
3 | 0.864 | 0.847 - 0.882 | 1 | “Veggie”
4 | 1.373 | 1.366 - 1.380 | 2 | “Cirrus”
5 | 1.61 | 1.59 - 1.63 | 1 | “Snow/Ice”
6 | 2.24 | 2.22 -2.27 | 2 | “Cloud Particle Size”
ABI: Bands 1-6 (Visible / NearIR)
Six visible or near visible bands on ABI, one on heritage imager
Notes: Based on Schmit et al, 2017. stars = today’s imager band.

## Slide 11: ABI Visible / Near IR Bands
Many thanks to Jordan Gerth, CIMSS
Current (legacy) GOES imagers: One visible band
GOES-R ABI:
  Two visible bands (1 km and 0.5 km)
  Near IR bands 1 or 2 km resolution
Benefits:
  Depiction of clouds
  Depiction of smoke
  Depiction of fog
  Used for AMV generation
  Used in snow cover estimates

## Slide 12: ABI Near-Infrared Bands
Current (legacy) GOES imagers: No near-infrared bands
GOES-R ABI: Four near-infrared bands, two at 1 km resolution, two at 2 km resolution
Benefits:
Depiction of vegetation health/coverage
Sharper coastlines and easier detection of inland river flooding
Easier cirrus cloud
Cloud-phase discrimination
Nocturnal fire detection

## Slide 13
ABI Band | Wavelength (µm) | Wavelength range (µm) | Sub-point pixel spacing (km) | Descriptive Name
7 | 3.90 | 3.80 - 3.99 | 2 | “Shortwave window”
8 | 6.19 | 5.79 - 6.59 | 2 | “Upper-level Water Vapor”
9 | 6.93 | 6.72 - 7.14 | 2 | “Mid-Level Water Vapor”
10 | 7.34 | 7.24 - 7.43 | 2 | “Lower/Mid-level Water Vapor”
11 | 8.44 | 8.23 - 8.66 | 2 | “Cloud-top Phase”
12 | 9.61 | 9.42 - 9.80 | 2 | “Ozone”
13 | 10.33 | 10.18 - 10.48 | 2 | “Clean longwave window”
14 | 11.21 | 10.82 - 11.60 | 2 | “Longwave window”
15 | 12.29 | 11.83 - 12.75 | 2 | “Dirty longwave window”
17 | 13.28 | 12.99 - 13.56 | 2 | “CO2”
ABI: Bands 7-16 (Infrared)
10 infrared bands on the ABI, four on heritage imager
Notes: Based on Schmit et al, 2017. stars = today’s imager band.

## Slide 14
ABI Spectral (IR) Bands
Credit: Mat Gunshor

## Slide 15: ABI Infrared Bands
Current GOES imagers: Four infrared bands
GOES-R ABI: 10 infrared bands, all at 2 km resolution
Benefits:
  Fire detection with better thermal signal
  Resolution of middle and upper tropospheric water vapor features
  Detection of sulfur dioxide and upper-atmosphere ozone
  Several window channels for discerning low-level water vapor gradients
  Clouds and Clouds phase
  Convection
  Atmospheric Motion and Atmospheric Moisture
  Volcanic plumes
  Ozone (and related PV)

## Slide 16: Question
How many spectral bands on the ABI?
a) 5
b) 16
c) 160
d) 1600

## Slide 17
0.47 mm
0.64 mm
0.86 mm
1.37 mm

## Slide 18
1.6 mm
2.2 mm
3.9 mm
6.2 mm

## Slide 19
6.9 mm
7.3 mm
8.4 mm
9.6 mm

## Slide 20
10.3 mm
11.2 mm
12.3 mm
13.3 mm

## Slide 35: Matching Action
https://cimss.ssec.wisc.edu/goes/webapps/matching/satmatch_abi_AZ1.html
Or other Band Matching links on the web page

## Slide 36
US Standard Atmosphere (1976)
Forward Model Used: RTTOV v11.3

## Slide 37
US Standard Atmosphere (1976)
Forward Model Used: RTTOV v11.3
GOES-16 ABI SRFs

## Slide 38
Forward Model Used: RTTOV v11.3
(Except 1000 DU of SO2 with PFAAST)
US Standard Atmosphere (1976) Brightness Temperature Difference
Caused By Removing Atmospheric Components
Notes: The SO2 plot

## Slide 39
US Standard Atmosphere (1976) Brightness Temperature Difference
Caused By Removing Atmospheric Components
Forward Model Used: RTTOV v11.3
(Except 1000 DU of SO2 with PFAAST)
GOES-16 ABI SRFs

## Slide 40: Question
Approximately how many ABI detectors are downloaded?
a) 16
b) 160
c) 1600
d) 8000
e) too many to count

## Slide 41: GOES-R ABI Weighting Functions
ABI has only 1 CO2 band, so upper-level temperature will be degraded compared to the current sounder

## Slide 42: Transmittance vs. Weighting Function

## Slide 43: Real Time Weighting Functions
http://cimss.ssec.wisc.edu/goes/wf
Notes: You can compute real-time weighting functions using actual radiosondes too (again, you’re assuming clear skies – which may not be true in reality). Including, if you click on the Non-USA Sites, radiosondes over central/South America (and Canada). Recently changed to inches for PW and C for the calculated temps.

## Slide 44: WF Action 1
http://cimss.ssec.wisc.edu/goes/wf/
Bring up the water vapor weighting functions from today and report the warmest water vapor band brightness temperature for a GOES ABI.

## Slide 45: WF Action 2
http://cimss.ssec.wisc.edu/goes/wf/examples/ABI/
Download and work on the ABI WF lab.

## Slide 46: Question
Approximately how large (in km) is the parallax from GOES for a 15 km high thunderstorm over Phoenix, AZ?
a) 0
b) 16
c) 22
d) 86
e) unknowable
Parallax is the apparent shift in an object's position (away from the sub-satellite point) as a result of viewing angle.

## Slide 47
Parallax
50,000 ft
(~15 km)
Cloud
The view of a high thunderstorm near St. Louis from an East GOES would have an apparent offset of approximately 18 km away from the satellite sub-point.
Thanks to Jim Nelson, CIMSS
Notes: Source: Jim Nelson

## Slide 48
The view of a high thunderstorm near St. Louis from a West GOES would have an apparent offset of approximately 30 km away from the satellite sub-point.
Parallax
50,000 ft
(~15 km)
Cloud
Thanks to Jim Nelson, CIMSS

## Slide 49: Temporal Spatial Action
http://cimss.ssec.wisc.edu/goes/webapps/temporal/
Pick a case, what time resolution do you prefer?

## Slide 50
CIRA Enhanced True Color 
 CIMSS Natural True Color
Notes: The CIRA variant is corrected for Rayleigh scattering with green produced from a look-up table.

## Slide 51: Red-Green-Blue (RGB) Composites
Many thanks to Jordan Gerth and Scott Lindstrom, CIMSS
Red-Green-Blue (RGB) composites are a way to visualize multiple bands in one image.
In order to interpret an RGB composite image, you must understand the contribution of the individual bands.
There are practically an infinite number of possible RGBs.
  It is possible to display any phenomena in any color.
  Don’t be tempted to correlate a feature with a color in your memory.

## Slide 52: The Birth of an RGB Composite
Scale a range of values for a single band from 0 to 1
Create a triplet at each pixel, where each of the three bands contributes a value to the triplet
The triplet is in the order of the additive primary colors for display purposes
  (Red, Green, Blue)
The triplet (1, 0, 0) is red, (0, 1, 0) is green, (0, 0, 1) is blue, (0, 0, 0) is black, and (1, 1, 1) is white

## Slide 53: RGB Color Space as a Cube
Source: https://en.wikipedia.org/wiki/RGB_color_space

## Slide 54: Educational RGB Webapp
Webapp to combine 3 ABI bands into one image.
Sample interactive “RGB” educational webapp using ABI images:
http://cimss.ssec.wisc.edu/education/apps/satrgb/FirstLightRGB.html
Notes: Tim Schmit, ASPB
https://ams.confex.com/ams/95Annual/webprogram/Paper265203.html ABI = Advanced Baseline Imager
Other new webapps: one to change both the spatial and temporal sampling and the other only the pixel sampling

## Slide 55: RGB Action
http://cimss.ssec.wisc.edu/goes/webapps/satrgb/overview_abi_goes16.html
Use GOES-16 ABI first light imagery to make a RGB to highlight cloud phase
Or
http://cimss.ssec.wisc.edu/goes/webapps/satrgb/satrgb_ABI_fd_realtime.html
Use GOES-16 ABI near realtime FD imagery to make a RGB to highlight cloud heights

## Slide 56: Question
The ABI can monitor:
a) fires
b) cloud top phase
c) the cryosphere
d) volcanic ash plumes
e) all of the above

## Slide 57
http://www.goes-r.gov
Many critical derived quantities

## Slide 58: GOES-16 Products
ABI L2+ Products
Cloud and Moisture Imagery (KPP)
Aerosol Detection (Smoke & Dust)
Aerosol Optical Depth (AOD)
Clear Sky Mask
Cloud Particle Size Distribution
Cloud Top Height
Cloud Top Phase
Cloud Top Pressure
Cloud Top Temperature
Derived Motion Winds
Derived Stability Indices
ABI L2+ Products (con’t)
Downward S/W Radiation: Surface
Fire/Hot Spot Characterization
Hurricane Intensity Estimation
Land Surface Temperature
Legacy Vertical Moisture Profile
Legacy Vertical Temperature Profile
Rainfall Rate/QPE
Reflected S/W Radiation: TOA
Sea Surface Temperature
Snow Cover
Total Perceptible Water
Volcanic Ash: Detection and Height
GLM L2 Product
Lightning: Events, Groups, Flashes
SEISS L1b Products
Energetic Heavy Ions
Magnetospheric e-/p+: Low Energy
Magnetospheric e-/p+: High Energy
Solar & Galactic Protons
EXIS L1b Product
Solar Flux: EUV
Solar Flux: X-ray Irradiance
SUVI L1b Product
Solar EUV Imagery
MAG L1b Product
Geomagnetic Field
ABI L1b Product
Radiances
Plus from the ABI (Pathfinders)
Aerosol Particle Size Cloud Layers/Heights Ice Thickness Low Cloud and Fog Ice: Concentration Ice: Motion

## Slide 59: TPW + Cloud Heights

## Slide 60
Conclusions
No other spacecraft observes over such a wide range of time and space scales
The next generation advanced geostationary imager continues the critical continuity of geostationary imagers
Large positive societal impacts, given its improved temporal, spatial, spectral and radiometric attributes; part of a global constellation
The ABI is improved, improved, improved and improved! Many quantitive derived products.

## Slide 62: GOES-17 Approximate Predicted Max FPM Temperature
Courtesy of: John Van Naarden (HARRIS Corporation)
Yaw flip
Yaw flip

## Slide 63: GOES-17 Meso-locations
POC: Tim Schmit, NESDIS Center for Satellite Applications and Research (Tim.J.Schmit@noaa.gov)

## Slide 64: Acknowledgements
The authors would like to thank the entire GOES and GOES-R teams; both within the government, industry and academia.
The views, opinions, and findings contained in this presentation are those of the authors and should not be construed as an official National Oceanic and Atmospheric Administration or U.S. Government position, policy, or decision.
GOES-16 / 17 data shown may be preliminary, experimental, during on-orbit testing.