Applications with New Multi-spectral Environmental Remote Sensing Satellites – Ostuni School

Menzel & Antonelli

Quiz 1

12 June 2006

Name:_________________________________________

1. The earth-atmosphere spectrum for a given scene is depicted in the figure below:

T   F    	The plateau between abscissa values 10.5 and 12 um is a window region of the atmosphere.

T   F	The tropopause temperature for this scene is roughly 220 K.

T   F  	In this scene, clouds are affecting the 7.5 to 8 um region of the spectrum and thus reducing

the brightness temperature.

T   F	For a clear scene BT(13.9 um) is typically colder than BT(13.3 um) because of CO2

absorption.

T   F	A given percentage increase in temperature produces a larger percentage increase in the

Planck 	radiance at 11 um than at 4 um.

2. If the albedo (cloudiness) of the earth increases from 33% to 50%, what is the corresponding change in the earth effective temperature (from 255 K to what)?.  Use Stefan’s law (irradiance is proportional to T4) to help you derive your answer.

3. In the scatter plot of BT(11um) on the x-axis and [r(1.6um)-r(.6um)] / [r(1.6um)+r(.6um)] on the y-axis, associate A, B, and C with the feature in the scene (draw a line to the best association)

snow covered land 				A

non snow covered land			B

cloud						C