## Slide 1
Recent Developments in CSPP Geo Software for Direct Broadcast
Graeme Martin, Liam Gumley, Nick Bearson, Jessica Braun, Geoff Cureton, Alan De Smet, Ray Garcia, Tommy Jasmin, Scott Mindock, Eva Schiffer, Kathy Strabala
University of Wisconsin – Madison, Space Science & Engineering Center /
Cooperative Institute for Meteorological Satellite Studies
American Meteorological Society 99th Annual Meeting
7 Jan 2019, Phoenix, Arizona

## Slide 2: Outline
Project Overview
Users
Software Packages
Future Plans

## Slide 3: What is CSPP Geo?
CSPP Geo = “Community Satellite Processing Package for Geostationary Data”
The CSPP Geo project creates and distributes software allowing direct broadcast users to create products from geostationary satellite data
The project draws on experience creating software allowing direct broadcast users to process data from polar orbiters (CSPP and IMAPP projects)
Funded by the GOES-R Program Office
Supported missions: GOES-16, GOES-17, Himawari-8, and GOES-15
Level 2 products are generated by algorithms that were developed for ABI under GOES-R AWG

## Slide 4: Software philosophy
CSPP Geo software is:
  Publicly available and free of charge: http://cimss.ssec.wisc.edu/csppgeo/
  Distributed as binary packages for 64-bit CentOS6-compatible Linux
  Distributed with all required 3rd party software bundled
  Easy to install and run
  Released with an optional test data package
  High level of user support
Software is intended to be run on rack-mounted commodity hardware
Recommended hardware specs for each software package are on the CSPP Geo website
Ancillary data is staged on servers at the U. of Wisconsin
Generally Level 2 software is developed in collaboration with scientists, while Level 1 software may be developed from scratch

## Slide 5: Project personnel and collaborators
The CSPP Geo team: Liam Gumley (Principal Investigator), Graeme Martin (Project Manager), Nick Bearson, Jessica Braun, Geoff Cureton, Alan DeSmet, Ray Garcia, Tommy Jasmin, Scott Mindock, Eva Schiffer, Kathy Strabala
NOAA / AIT: Walter Wolf, Shanna Sampson, Tom King and team
GEOCAT: Mike Pavolonis
GOES-R Cloud team: Andy Heidinger (lead), Denis Botambekov, Corey Calvert, Pat Heck, William Straka, Andy Walther, Steve Wanzong
Imagery: Tim Schmit, Kaba Bah, Jordan Gerth, Mat Gunshor

## Slide 6
CSPP Geo software is used at half of all GRB receiving stations around the world (as of early 2018, per GRB User Group survey)
Users include NOAA / NWS, NASA, international meteorological agencies, receiving station vendors, data and weather service providers, and the university and research community

## Slide 7
CSPP Geo software is used at half of all GRB receiving stations around the world (as of early 2018, per GRB User Group survey)
Users include NOAA / NWS, NASA, international meteorological agencies, receiving station vendors, data and weather service providers, and the university and research community
Credit: Jim McNitt

## Slide 8: CSPP Geo Software
Himawari AHI
GOES-16/17
GOES-15

## Slide 9: GOES-16
GOES-16 is the first of a new generation of U.S. geostationary satellites
Launched in November 2016
GOES-16 is now the operational GOES-East satellite, located at W 75.2° since Dec 2017
  Location during checkout was W 89.5°
GOES-16 has a direct broadcast stream called GOES Rebroadcast (GRB)
  Includes data from all GOES-16 instruments
GRB receiving systems are currently available from vendors
NOAA provides information on GRB including a list of receiving station vendors at http://www.goes-r.gov/
Advanced Baseline Imager (ABI)
Geostationary Lightning Mapper (GLM)
Solar Ultraviolet Imager (SUVI)
Space Environment In-Situ Suite (SEISS)
Extreme Ultraviolet and X-ray Irradiance Sensors (EXIS)
Magnetometer (MAG)
GOES-16 instruments:

## Slide 10: GOES-16 L1B observed data volumes
 | GOES 13/15 (GVAR) | GOES-16 (GRB)
Data rate | 2.1 Mbps | 31 Mbps
Raw data volume | 21.5 GB/day | 310 GB/day
Raw data volume (idle / null data removed) | 14.24 GB/day | 99 GB/day (Mode 3) 150 GB/day (Mode 4)
Based on representative samples of data volumes observed at
U. Wisconsin GRB receiving station during PLT
uncompressed | 550GB/day (Mode 3)
compressed | 135-140 GB/day (Mode 3) 215 GB/day (Mode 4)
ABI L1B Products (NetCDF):
Raw data:

## Slide 11: The GRB Software Package
Runs as a server, processing the raw GRB data stream
  reads CADUs from two sockets
Ingestor component is a modified version of NASA RT-STPS
Extracts data payloads, decompresses, reconstructs datasets as they were created on the Ground Segment
Generates products from all GOES-R instruments
  Level 1 ABI and space weather, Level 2 GLM
Requires multiple cores, hardware specs published on website
Includes an experimental tracking interface allowing data to be used as it arrives

## Slide 12: GRB Software – Year in Review
Release Date | Version | Description
June 2018 | GRB v0.4.7 | Changes for update to ground system
Aug 2018 | GRB v1.0.14 | initial V1.0 release of GRB package including provisional support for G-17 and ABI Mode 6, UDP multicast support, robustness and performance improvements, logging and interface improvements
Oct 2018 | GRB v1.0.15 | Changes for DO.07 update to ground system
Dec 2018 | GRB v1.0.18 | Cumulative bug fixes, minor improvements
Jan 2019 | GRB v1.0.19 | Changes for DO.07.01 update to ground system (planned live date is Jan 15, 2019)
5 software releases in the last year
3 releases to support changes to the GOES-R ground system
v1.0 milestone
Participated in GOES-17 PLT
Participated in GRB User Group and reported issues affecting GRB to program

## Slide 13
CSPP Geo ABI quicklooks
GOES-16
GOES-17
Preliminary, Non-Operational Data
Notes: GOES-East location = 75.2W

## Slide 14: The AIT Framework Software Package
Further processes ABI L1B data to generate Level 2 products
Core processing software was developed by the Algorithm Integration Team at NOAA STAR as an integration point for research implementations of GOES-R Level 2 research algorithm
Software was developed at UW for Imagery generation, data conversion, quicklooks, ancillary download and infrastructure
Beta version was released 5 Jan, 2018
  Generates a subset of the GOES-R Baseline products
  Software, documentation and test data are available from the CSPP Geo website
Aerosol Detection: Smoke and Dust
Aerosol Optical Depth
Clear Sky Masks
Cloud and Moisture Imagery
Cloud Optical Depth (day/night)
Cloud Particle Size Distribution (day/night)
Cloud Top Height
Cloud Top Phase
Cloud Top Pressure
Cloud Top Temperature
Land Surface Temperature (Skin)
Initial set of products:

## Slide 15: AIT Framework v1.0 and beyond
V1.0 release is planned for early 2019
Version 1.0 changes will include
  Updated product algorithms, LUTs and static ancillary data
  Bug fixes
  User interface improvements
  Segmentation overlap
  Parallelization tuned for target architecture
  Logging improvements
  Robustness and performance improvements
  HTTPS ancillary data download
Post-V1.0: will add support for GOES-17, and additional products
Products have been identified as high priority to users and targeted for release
  Rainfall Rate / QPE
  Sea Surface Temperature (Skin)
  Low Cloud and Fog
  Cloud Cover Layers
Release timeline will depend on availability of algorithms / GOES-17 support, targeting mid-late 2019.

## Slide 16: AIT Framework Quicklooks

## Slide 17: Geo2Grid Software Package
Will generate high quality imagery from GOES-16 ABI and Himawari AHI data
  ”composite RGB” images (true color, natural color, airmass, ash, dust, fog, night microphysics)
  per-band images
Formats: geo-tiff and PNG with coastlines
Uses open source “satpy” plotting library
Users can define grids (projections, resolutions and coverage)
Version 1.0 planned for early 2019
Presentation 6B.3: “Shouldn't This Be Easy? NOAA Open Source Software For Creating High Quality Satellite Images”
David Hoese, Tuesday, January 08, 2019 , 3:30PM, North 131C

## Slide 18
Geo2Grid true color images include
  Rayleigh correction
  Artificial green band
  Sharpening to 500m
  Solar zenith angle correction
  Enhancement (logarithmic stretching to bands)

## Slide 19
Geo2Grid
Full Disk
True Color
2017-09-20
1730z

## Slide 24
Geo2Grid
Full Disk
True Color
2017-09-20
1730z

## Slide 29
GOES-16 “Natural Color” RGB image generated by CSPP Geo software.
Displayed in Real Earth: http://realearth.ssec.wisc.edu/

## Slide 30: The GEOCAT Level 2 Software Package for AHI and GOES-15
Initial set of products:
GEOCAT = “Geostationary Cloud Algorithm Testbed”
Originally developed by NOAA Scientist Mike Pavolonis for GOES-R algorithm development
Products are generated by research versions of GOES-R algorithms that have been updated and adapted for the Japanese ABI-class instrument “AHI”
CSPP Geo team integrated updated algorithms for AHI, developed “glue” code
Parallel processing is needed to keep up with the data rate
V1.0 beta was released in Fall 2016
Cloud and Moisture Imagery
Clear Sky Masks
Cloud Phase
Cloud Type
Cloud Top Height
Cloud Top Pressure
Cloud Top Temperature
Cloud Optical Depth (day/night)
Cloud Particle Size Distribution (day/night)
Cloud Liquid Water Path (day/night)
Cloud Ice Water Path (day/night)
Low Cloud and Fog
Poster 237: Himawari Support in the CSPP-GEO Direct Broadcast Package
Geoff Cureton, Monday, January 07, 2019, 4PM - 6PM, Hall 4

## Slide 31: Other software
Ruth.Monarrez@jpl.nasa.gov
Himawari Ingest Library
Reads AHI data in HSD and HRIT formats, transparently handling datasets spanning multiple files
Used in multiple programs maintained at U. of Wisconsin
Open source gitlab repo
AXI-Tools
Generates tiled / SCMI products from ABI and AHI radiances
Creates ABI CMIP product in mission-standard format
Open source Gitlab repo
Used by NWS to load AHI data into AWIPS
GRB data converted to SCMI and displayed in AWIPS2
AHI data converted with libHimawari and loaded in AWIPS2

## Slide 32: Future
Plans for 2019
  AIT Framework: V1 release, added products, GOES-17 support
  Geo2Grid: V1 release
  GEOCAT: V1 release
  GRB package: continued maintenance
New development is contingent on new funding:
  Continued release of Level 2 products for ABI, AHI
  Support for future missions and instruments
  GLM and space weather visualization capabilities
  Higher level GLM products
  Monitoring tools
  Data subsetting
  Support for low-latency streaming

## Slide 34: For more information on CSPP Geo…
Further information
website: http://cimss.ssec.wisc.edu/csppgeo/
email: csppgeo.issues@ssec.wisc.edu
At AMS 2019
Booth 233: SSEC / Univ. of Wisconsin
Presentation 6B.3: “Shouldn't This Be Easy? NOAA Open Source Software For Creating High Quality Satellite Images” David Hoese, Tuesday, January 08, 2019 , 3:30PM, North 131C
Poster 237: “Himawari Support in the CSPP-GEO Direct Broadcast Package”, Geoff Cureton, Monday, January 07, 2019, 4PM - 6PM, Hall 4