## Slide 1: ProbSevere – A New Tool for NWS Severe Weather Warning Operations
Michael J. Pavolonis (NOAA/NESDIS)
John Cintineo (UW-CIMSS)
Justin Sieglaff (UW-CIMSS)
Dan Lindsey (NOAA/NESDIS)
Lee Cronce (UW-CIMSS)

## Slide 2
Data to Environmental Intelligence
Storm Environment
High-resolution NWP Data
Satellite Imagery and Derived Products
Radar Imagery and Derived Products
Evolution of Cumulus to Cumulonimbus
Storm Tracking and Hydrometeor Properties
Total Lightning
Storm Electrification
Probability a thunderstorm will produce severe weather in the future (up to 60 minutes)
Notes: A few more details about the input data into the statistical model are beneficial. The high-resolution NWP data are used to characterize the instability and shear of the environment a storm develops.
The satellite imagery is used in two ways; to track clouds across space and time—in the same way a human views satellite imagery loops and to quantify the cloud growth rates, which are used as predictors in the model.
The radar data are used in a similar manner as the satellite data. The radar data are used to track storm cells in reflectivity imagery—again like how a meteorologist looks at a loop of radar imagery. And to quantify the intensity of the precipitation core of a developing thunderstorm, which is used as a predictor in the model.
The total lightning data are used to quantify the number of lightning flashes per minute within a radar tracked storm cell.
Before discussing a few more details about the input datasets, a schematic of how the statistical model works is presented in the following slide.
.

## Slide 3
“Big Data” to Environmental Intelligence
1). Mesoscale NWP
Effective Bulk Shear
Most Unstable CAPE
Short-term forecasts from the Rapid Refresh NWP model are used to characterize the dynamic and thermodynamic environment.
Notes: The bulk vector difference from the effective inflow base upward to 50% of the equilibrium level height for the most unstable parcel in the lowest 300 mb. This parameter is similar to the 0-6 km bulk shear, though it accounts for storm depth (effective inflow base to EL) and is designed to identify both surface-based and "elevated" supercell environments. Supercells become more probable as the effective bulk shear vector increases in magnitude through the range of 25-40 kt and greater.
MUCAPE (Most Unstable Convective Available Potential Energy) is a measure of instability in the troposphere. This value represents the total amount of potential energy available to the most unstable parcel of air found within the lowest 300-mb of the atmosphere while being lifted to its level of free convection (LFC). No parcel entrainment is considered. The CAPE and CIN calculations use the virtual temperature correction.
The LPL (Lifted Parcel Level) allows for the determination of the height of the most unstable parcel. This makes it easy to identify areas where the largest CAPE is "elevated."

## Slide 4
“Big Data” to Environmental Intelligence
2). Geostationary Satellite Data
False Color Image
Top of Troposphere Emissivity
(Pavolonis, 2010)
Developing Convection
Developing Convection
Texas
Texas
Object are extracted from εtot(11μm) and are tracked in time (Lakshmanan et al. 2003). Time trends in the maximum value of εtot(11μm) are utilized.
Notes: Tracking algorithm: Lakshmanan et al. 2003

## Slide 5
“Big Data” to Environmental Intelligence
2). Geostationary Satellite Data
False Color Image
IR-derived Cloud Top Phase
(Pavolonis, 2010)
Developing Convection
Developing Convection
Texas
Texas
The time trend in the fraction of glaciated pixels within each object is also utilized.

## Slide 6
“Big Data” to Environmental Intelligence
3). Precipitation RADAR Data
MESH
The MESH is taken from the Multi-sensor/Multi-radar System (MRMS) (Witt el al., 1998; Lakhmanan et al., 2006). The composite MRMS reflectivity is used to identify and track radar objects.
Notes: Thermally weighted integration of reflectivity

## Slide 7
“Big Data” to Environmental Intelligence
4). Lightning Data
Total Lightning
Liu and Heckman, 2012
Total lightning (per minute) within each radar object is utilized. The total lightning data are from Earth Networks.
Notes: Same concept can be applied to GEO lightning sensor data

## Slide 8
Automated integration of information
A meteorologist sees developing storms and cloud clusters—not satellite pixels or radiances.
The same concepts apply to radar data.
Meteorologists view cells or storms—so the computer needs to identify and track radar cells and their evolution over time.
Notes: -Extract storm-scale objects and track them in time
-Instantaneous satellite-derived cloud fields are not well-suited to the short-term severe weather forecasting, but temporal trends in those cloud properties are.
-Calculating temporal trends in satellite-derived cloud properties is not a trivial task.
-In order to capture temporal trends in cloud properties, object tracking is needed
-Collaboration with OU-CIMMS and NSSL was essential
-Model output is updated after every radar and satellite scan

## Slide 9
ProbSevere Model AWIPS-II Display
Model output are shapefiles contoured around radar storm cells.
Enhancement designed for overlay on radar reflectivity—but can be overlaid on any field (satellite, radar velocity, etc.).
Sampling offers readout of model probability as well as each model input.
Notes: We will now transition from discussing how the statistical model works and learning about the input datasets to showing examples of how the model performed in some severe weather events.
The model output is displayed in two ways. One is a probability contour with a color enhancement designed for overlay on top of typical radar reflectivity color tables (e.g. greens, yellows, and reds are avoided in the ProbSevere colortable). The shapefile nature of the output makes the display very flexible—the contours can be overlaid on any field within AWIPS-II (e.g., radar velocity). Additionally, the model probability and each model predictor is displayed as text when sampling is turned on. The following bullets briefly describe the text read-out.
This field is the ProbSevere probability and ranges between 0 and 100% for a given storm cell.
This field is the most unstable CAPE from our RAP composite for the storm cell.
This field is the effective bulk shear from our RAP composite for the storm cell.
This field is the MRMS MESH value—the time and value are provided. Note the MRMS may not match a single radar site MESH algorithm—both time and value.
This field is the normalized vertical growth rate of the storm. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are percentage of the troposphere depth the cloud grew per minute. The exact values are not terribly important—we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the glaciation rate or the rate at which the storm-top transitioned from liquid water droplets to ice crystals. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are a percentage of water to ice conversion per minute. Again we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the flash rate--the time and value are provided. Recall the total lightning is part of a 2-D predictor in the ProbSevere model—combining effective bulk shear and total lightning flash rate.
While each model predictor is provided in the text read-out, it is important to emphasize—the sum of the information--the probability--is more valuable than any individual piece of information.

## Slide 10
ProbSevere Model AWIPS-II Display
SVR Prob: ProbSevere probability 0-100%.
Notes: We will now transition from discussing how the statistical model works and learning about the input datasets to showing examples of how the model performed in some severe weather events.
The model output is displayed in two ways. One is a probability contour with a color enhancement designed for overlay on top of typical radar reflectivity color tables (e.g. greens, yellows, and reds are avoided in the ProbSevere colortable). The shapefile nature of the output makes the display very flexible—the contours can be overlaid on any field within AWIPS-II (e.g., radar velocity). Additionally, the model probability and each model predictor is displayed as text when sampling is turned on. The following bullets briefly describe the text read-out.
This field is the ProbSevere probability and ranges between 0 and 100% for a given storm cell.
This field is the most unstable CAPE from our RAP composite for the storm cell.
This field is the effective bulk shear from our RAP composite for the storm cell.
This field is the MRMS MESH value—the time and value are provided. Note the MRMS may not match a single radar site MESH algorithm—both time and value.
This field is the normalized vertical growth rate of the storm. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are percentage of the troposphere depth the cloud grew per minute. The exact values are not terribly important—we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the glaciation rate or the rate at which the storm-top transitioned from liquid water droplets to ice crystals. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are a percentage of water to ice conversion per minute. Again we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the flash rate--the time and value are provided. Recall the total lightning is part of a 2-D predictor in the ProbSevere model—combining effective bulk shear and total lightning flash rate.
While each model predictor is provided in the text read-out, it is important to emphasize—the sum of the information--the probability--is more valuable than any individual piece of information.

## Slide 11
ProbSevere Model AWIPS-II Display
Env MUCAPE: RAP composite MUCAPE for storm environment.
Notes: We will now transition from discussing how the statistical model works and learning about the input datasets to showing examples of how the model performed in some severe weather events.
The model output is displayed in two ways. One is a probability contour with a color enhancement designed for overlay on top of typical radar reflectivity color tables (e.g. greens, yellows, and reds are avoided in the ProbSevere colortable). The shapefile nature of the output makes the display very flexible—the contours can be overlaid on any field within AWIPS-II (e.g., radar velocity). Additionally, the model probability and each model predictor is displayed as text when sampling is turned on. The following bullets briefly describe the text read-out.
This field is the ProbSevere probability and ranges between 0 and 100% for a given storm cell.
This field is the most unstable CAPE from our RAP composite for the storm cell.
This field is the effective bulk shear from our RAP composite for the storm cell.
This field is the MRMS MESH value—the time and value are provided. Note the MRMS may not match a single radar site MESH algorithm—both time and value.
This field is the normalized vertical growth rate of the storm. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are percentage of the troposphere depth the cloud grew per minute. The exact values are not terribly important—we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the glaciation rate or the rate at which the storm-top transitioned from liquid water droplets to ice crystals. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are a percentage of water to ice conversion per minute. Again we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the flash rate--the time and value are provided. Recall the total lightning is part of a 2-D predictor in the ProbSevere model—combining effective bulk shear and total lightning flash rate.
While each model predictor is provided in the text read-out, it is important to emphasize—the sum of the information--the probability--is more valuable than any individual piece of information.

## Slide 12
ProbSevere Model AWIPS-II Display
Env EBShear: RAP composite effective bulk shear for storm environment.
Notes: We will now transition from discussing how the statistical model works and learning about the input datasets to showing examples of how the model performed in some severe weather events.
The model output is displayed in two ways. One is a probability contour with a color enhancement designed for overlay on top of typical radar reflectivity color tables (e.g. greens, yellows, and reds are avoided in the ProbSevere colortable). The shapefile nature of the output makes the display very flexible—the contours can be overlaid on any field within AWIPS-II (e.g., radar velocity). Additionally, the model probability and each model predictor is displayed as text when sampling is turned on. The following bullets briefly describe the text read-out.
This field is the ProbSevere probability and ranges between 0 and 100% for a given storm cell.
This field is the most unstable CAPE from our RAP composite for the storm cell.
This field is the effective bulk shear from our RAP composite for the storm cell.
This field is the MRMS MESH value—the time and value are provided. Note the MRMS may not match a single radar site MESH algorithm—both time and value.
This field is the normalized vertical growth rate of the storm. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are percentage of the troposphere depth the cloud grew per minute. The exact values are not terribly important—we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the glaciation rate or the rate at which the storm-top transitioned from liquid water droplets to ice crystals. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are a percentage of water to ice conversion per minute. Again we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the flash rate--the time and value are provided. Recall the total lightning is part of a 2-D predictor in the ProbSevere model—combining effective bulk shear and total lightning flash rate.
While each model predictor is provided in the text read-out, it is important to emphasize—the sum of the information--the probability--is more valuable than any individual piece of information.

## Slide 13
ProbSevere Model AWIPS-II Display
MRMS MESH: Storm maximum MESH. Time and size (inches).
Notes: We will now transition from discussing how the statistical model works and learning about the input datasets to showing examples of how the model performed in some severe weather events.
The model output is displayed in two ways. One is a probability contour with a color enhancement designed for overlay on top of typical radar reflectivity color tables (e.g. greens, yellows, and reds are avoided in the ProbSevere colortable). The shapefile nature of the output makes the display very flexible—the contours can be overlaid on any field within AWIPS-II (e.g., radar velocity). Additionally, the model probability and each model predictor is displayed as text when sampling is turned on. The following bullets briefly describe the text read-out.
This field is the ProbSevere probability and ranges between 0 and 100% for a given storm cell.
This field is the most unstable CAPE from our RAP composite for the storm cell.
This field is the effective bulk shear from our RAP composite for the storm cell.
This field is the MRMS MESH value—the time and value are provided. Note the MRMS may not match a single radar site MESH algorithm—both time and value.
This field is the normalized vertical growth rate of the storm. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are percentage of the troposphere depth the cloud grew per minute. The exact values are not terribly important—we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the glaciation rate or the rate at which the storm-top transitioned from liquid water droplets to ice crystals. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are a percentage of water to ice conversion per minute. Again we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the flash rate--the time and value are provided. Recall the total lightning is part of a 2-D predictor in the ProbSevere model—combining effective bulk shear and total lightning flash rate.
While each model predictor is provided in the text read-out, it is important to emphasize—the sum of the information--the probability--is more valuable than any individual piece of information.

## Slide 14
ProbSevere Model AWIPS-II Display
Norm Vert Growth Rate (Max): Maximum storm cell satellite vertical growth rate.
Time occurred, normalized vertical cloud growth rate per minute.
Classified as weak, moderate, or strong.
Notes: We will now transition from discussing how the statistical model works and learning about the input datasets to showing examples of how the model performed in some severe weather events.
The model output is displayed in two ways. One is a probability contour with a color enhancement designed for overlay on top of typical radar reflectivity color tables (e.g. greens, yellows, and reds are avoided in the ProbSevere colortable). The shapefile nature of the output makes the display very flexible—the contours can be overlaid on any field within AWIPS-II (e.g., radar velocity). Additionally, the model probability and each model predictor is displayed as text when sampling is turned on. The following bullets briefly describe the text read-out.
This field is the ProbSevere probability and ranges between 0 and 100% for a given storm cell.
This field is the most unstable CAPE from our RAP composite for the storm cell.
This field is the effective bulk shear from our RAP composite for the storm cell.
This field is the MRMS MESH value—the time and value are provided. Note the MRMS may not match a single radar site MESH algorithm—both time and value.
This field is the normalized vertical growth rate of the storm. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are percentage of the troposphere depth the cloud grew per minute. The exact values are not terribly important—we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the glaciation rate or the rate at which the storm-top transitioned from liquid water droplets to ice crystals. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are a percentage of water to ice conversion per minute. Again we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the flash rate--the time and value are provided. Recall the total lightning is part of a 2-D predictor in the ProbSevere model—combining effective bulk shear and total lightning flash rate.
While each model predictor is provided in the text read-out, it is important to emphasize—the sum of the information--the probability--is more valuable than any individual piece of information.

## Slide 15
ProbSevere Model AWIPS-II Display
Glaciation rate (Max): Maximum storm cell satellite glaciation rate.
Time occurred, percentage of conversion from water to ice cloud-tops per minute. Classified as weak, moderate, or strong.
Notes: We will now transition from discussing how the statistical model works and learning about the input datasets to showing examples of how the model performed in some severe weather events.
The model output is displayed in two ways. One is a probability contour with a color enhancement designed for overlay on top of typical radar reflectivity color tables (e.g. greens, yellows, and reds are avoided in the ProbSevere colortable). The shapefile nature of the output makes the display very flexible—the contours can be overlaid on any field within AWIPS-II (e.g., radar velocity). Additionally, the model probability and each model predictor is displayed as text when sampling is turned on. The following bullets briefly describe the text read-out.
This field is the ProbSevere probability and ranges between 0 and 100% for a given storm cell.
This field is the most unstable CAPE from our RAP composite for the storm cell.
This field is the effective bulk shear from our RAP composite for the storm cell.
This field is the MRMS MESH value—the time and value are provided. Note the MRMS may not match a single radar site MESH algorithm—both time and value.
This field is the normalized vertical growth rate of the storm. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are percentage of the troposphere depth the cloud grew per minute. The exact values are not terribly important—we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the glaciation rate or the rate at which the storm-top transitioned from liquid water droplets to ice crystals. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are a percentage of water to ice conversion per minute. Again we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the flash rate--the time and value are provided. Recall the total lightning is part of a 2-D predictor in the ProbSevere model—combining effective bulk shear and total lightning flash rate.
While each model predictor is provided in the text read-out, it is important to emphasize—the sum of the information--the probability--is more valuable than any individual piece of information.

## Slide 16
ProbSevere Model AWIPS-II Display
Flash Rate: Total lightning flash rate within radar object. Time and flash rate (flashes / min).
Notes: We will now transition from discussing how the statistical model works and learning about the input datasets to showing examples of how the model performed in some severe weather events.
The model output is displayed in two ways. One is a probability contour with a color enhancement designed for overlay on top of typical radar reflectivity color tables (e.g. greens, yellows, and reds are avoided in the ProbSevere colortable). The shapefile nature of the output makes the display very flexible—the contours can be overlaid on any field within AWIPS-II (e.g., radar velocity). Additionally, the model probability and each model predictor is displayed as text when sampling is turned on. The following bullets briefly describe the text read-out.
This field is the ProbSevere probability and ranges between 0 and 100% for a given storm cell.
This field is the most unstable CAPE from our RAP composite for the storm cell.
This field is the effective bulk shear from our RAP composite for the storm cell.
This field is the MRMS MESH value—the time and value are provided. Note the MRMS may not match a single radar site MESH algorithm—both time and value.
This field is the normalized vertical growth rate of the storm. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are percentage of the troposphere depth the cloud grew per minute. The exact values are not terribly important—we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the glaciation rate or the rate at which the storm-top transitioned from liquid water droplets to ice crystals. It is the maximum value attained during the growth stage of the storm and the time that maximum value occurred. The units are a percentage of water to ice conversion per minute. Again we append a statistical measure of intensity with the terms “weak”, “moderate”, or “strong”.
This field is the flash rate--the time and value are provided. Recall the total lightning is part of a 2-D predictor in the ProbSevere model—combining effective bulk shear and total lightning flash rate.
While each model predictor is provided in the text read-out, it is important to emphasize—the sum of the information--the probability--is more valuable than any individual piece of information.

## Slide 17
08 May 2014
Notes: Now getting to examples, the first example is over southeastern South Dakota on the western edge of a slight risk region as depicted by the Storm Prediction Center outlook.

## Slide 18
1644 UTC May-08-2014
IA
SD
MUCAPE ~ 750 J kg-1
Eff. shear ~ 48 kts
Prob = 27%
Highly sheared environment
Low MESH
Low lightning
Notes: In these examples, MRMS composite reflectivity is shaded and the ProbSevere contours are overlaid on the reflectivity data with the text read-out provided for the storm of interest. At 1644UTC a developing storm had marginal instability but significant shear. The probability at this time was low—only 27% as the MRMS MESH and total lightning were fairly low.

## Slide 19
1646 UTC May-08-2014
SD
MUCAPE ~ 750 J kg-1
Eff. shear ~ 48 kts
Prob = 54%
Strong satellite growth and glaciation rates.
Small increase in lightning.
IA
Notes: At 1646 UTC, satellite growth rates were diagnosed and included into the ProbSevere calculation. Both the vertical growth rate and glaciation rate were in the ‘strong’ category, which drove the probability up to 54%.

## Slide 20
1648 UTC May-08-2014
SD
MUCAPE ~ 750 J kg-1
Eff. shear ~ 48 kts
Prob = 78%
Strong satellite growth and glaciation rates.
MESH increases to 0.89”.
Lightning continues to increase.
IA
Notes: Two minutes later, the storm continued to intensify as indicated by the MESH and total lightning read-outs. The probably again jumped, now to 78%.

## Slide 21
1726 UTC May-08-2014
SD
MUCAPE ~ 750 J kg-1
Eff. shear ~ 48 kts
Prob = 85%
KFSD issues SVR warning @ 1726 UTC (40 minutes)
Golf ball sized hail report @ 1732 UTC (46 minutes)
IA
Notes: The storm continued to exhibit high probabilities and at 1726 UTC a severe thunderstorm warning was issued by the Sioux Falls WFO. 6 minutes later the first severe report of golf ball sized hail was received. This example demonstrates how ProbSevere can be used to identify a storm that is likely to produce severe weather and potentially be used to increase lead-time. [For those interested, the storms over extreme northwestern Iowa/southwestern MN had lower probabilities and did not produce severe reports.]

## Slide 22
1646 UTC May-08-2014
Impact of GOES Data
NWP + Satellite + Radar + Lightning
NWP + Satellite + Radar + Lightning
Prob = 54%
Prob = 27%
Time (UTC) | With GOES | Without GOES
1644 | 27% (no sat. growth yet) | 27%
1646 | 54% | 27%
1648 | 78% | 54%
1728 | 85% | 65%
Notes: We are often asked, what value do the satellite growth rates provide? Using this example, you can see at 1646 UTC, by removing the satellite observations, the ProbSevere probability is reduced by HALF! Additionally, removing the satellite growth rates reduces the amount of lead-time gained.

## Slide 23
ProbSevere – Without Lightning
31 min
19 min
Notes: A validation for about 5000 storms on 18 convectively active days during 2014 was performed. (Using manual analysis from Eric)

## Slide 24
ProbSevere – With Lightning
19 min
33 min
Notes: A validation for about 5000 storms on 18 convectively active days during 2014 was performed. (Using manual analysis from Eric)

## Slide 25
ProbSevere – With Lightning
Once a 60% probability is achieved, any gain in CSI at higher probabilities is negligible
Overall, the ProbSevere probabilities are well calibrated
Over-forecast
Under-forecast

## Slide 26
CAPE 0-1500 J/Kg
CAPE 1500-2500 J/Kg
CAPE 2500+ J/Kg
EBS 0-10 m/s
EBS 10-15 m/s
EBS 15+ m/s
Small Sample Size
Small Sample Size
Reliability – With Lightning
Notes: Validation using ALL storm reports (not just the first)
total_sev_storms= 71 156 181 85 132 69 85 200 110 total_ns_storms= 8328 6667 6124 2090 1381 589 855 773 329

## Slide 27
Analysis of Daily Storm Tracks

## Slide 28
Analysis of Daily Storm Tracks

## Slide 29
Analysis of Daily Storm Tracks

## Slide 30
May 5, 2016

## Slide 31
Nevada
California
May 5, 2016

## Slide 32
Wind report associated with storm highlighted by ProbSevere

## Slide 33
June 8, 2016

## Slide 34
Washington
Oregon
Idaho
June 8, 2016

## Slide 35
64% @ 20:00Z
Tornado @ 20:22Z
Golf ball sized hail @ 20:30Z
65% @ 20:38Z
1’’ hail @ 21:24Z
2’’ hail @ 21:45Z
83% @ 21:08Z
1.25’’ hail @ 21:45Z
June 8, 2016
Notes: 22 minutes
37 minutes
46 minutes

## Slide 36
Oregon
Idaho
Washington

## Slide 37
June 13, 2016

## Slide 38
June 13, 2016

## Slide 39
57% @ 18:02Z
1’’ hail @ 18:20Z
Golf ball sized hail @ 18:37Z
June 13, 2016
Notes: 18 minutes

## Slide 40
June 11, 2016
Region of Interest

## Slide 41
Salt Lake City
Verified severe storm with no ProbSevere object
June 11, 2016 – Beam Blockage
Arizona
Nevada
Utah

## Slide 42
Hazardous Weather Testbed (HWT)
http://goesrhwt.blogspot.com
Notes: HWT: NSSL, SPC, and the Norman WFO
-During multiple experiments that take place in the HWT throughout the year, researchers and forecasters work side-by-side to evaluate emerging research concepts and tools in simulated operational settings, including experimental forecast and warning generation exercises.

## Slide 43: 2016 HWT

## Slide 44: 2016 HWT
Notes: Sometimes delicately worded criticisms.

## Slide 45
Underestimated MESH? (April 27, 2016)
Notes: -Underestimated MESH will be most costly when lightning activity is also low.
-NSSL and OU-CIMMS are investigating the impact of radar scanning and the operational settings used to merge data from multiple radars

## Slide 46: Continued Development
NWP
HRRR
SPC-OA
SREF
GOES-R
Super-rapid scan
GLM
Cb properties
Create more refined and specific forecasts of severe weather (tornado, hail, wind)
Images are from NOAA, NASA, UW-CIMSS, and OU-CIMMS
NEXRAD
Dual-pol products
Doppler velocities
Other
Global lightning
Additional radars
Notes: -Working on training several versions of the model to account for differing physical mechanisms that produce severe wind.
-Create several models to account for different physical mechanisms for producing different types of severe weather

## Slide 47
ProbSevere
EMC
Input: 1300 MB
File size: 0.2 MB
OUTPUT
1 set of RAP grids
30 CONUS radar scans
8 CONUS satellite scans (in rapid scan)
30 output files
ProbSevere Model Real-Time Operations
Satellite, radar, lightning, and model data have different timescales
ProbSevere probabilities can change each time new data are available
In one hour…
30 lightning files
Notes: So how is all this information combined in real-time processing? Unlike most GOES-R related projects that update with each satellite scan—ProbSevere is different. The model updates at the frequency of the MRMS radar data—about every 2 minutes.
When a storm develops and is tracked within satellite imagery, it has information about the storm environment from the RAP composite—which updates every hour. The probabilities are computed for every set of MRMS radar data—about every 2 minutes. The ENI total lightning data is also updated every 2 minutes. The update frequency of the current GOES satellite in routine scan mode is every 15 minutes, or roughly every 7.5 minutes in rapid-scan mode.
The critical point is:
The model does not wait on a satellite scan—it uses the most recent information available from satellite—whether the satellite is in routine scan mode or rapid scan mode. So users should expect updates in AWIPS-II about every 2 minutes.

## Slide 48
ProbSevere
EMC
File size: 0.2 MB
OUTPUT
1 set of RAP grids
30 CONUS radar scans
8 CONUS satellite scans (in rapid scan)
30 output files
ProbSevere Model Real-Time Operations
Satellite, radar, lightning, and model data have different timescales
ProbSevere probabilities can change each time new data are available
In one hour…
30 lightning files
Input: 9000 MB
With 1 GOES-R ABI
Notes: So how is all this information combined in real-time processing? Unlike most GOES-R related projects that update with each satellite scan—ProbSevere is different. The model updates at the frequency of the MRMS radar data—about every 2 minutes.
When a storm develops and is tracked within satellite imagery, it has information about the storm environment from the RAP composite—which updates every hour. The probabilities are computed for every set of MRMS radar data—about every 2 minutes. The ENI total lightning data is also updated every 2 minutes. The update frequency of the current GOES satellite in routine scan mode is every 15 minutes, or roughly every 7.5 minutes in rapid-scan mode.
The critical point is:
The model does not wait on a satellite scan—it uses the most recent information available from satellite—whether the satellite is in routine scan mode or rapid scan mode. So users should expect updates in AWIPS-II about every 2 minutes.

## Slide 49
ProbSevere
EMC
File size: 0.2 MB
OUTPUT
1 set of RAP grids
30 CONUS radar scans
8 CONUS satellite scans (in rapid scan)
30 output files
ProbSevere Model Real-Time Operations
Satellite, radar, lightning, and model data have different timescales
ProbSevere probabilities can change each time new data are available
In one hour…
30 lightning files
Input: 12,500 MB
With 1 GOES-R ABI +
HRRR
Notes: So how is all this information combined in real-time processing? Unlike most GOES-R related projects that update with each satellite scan—ProbSevere is different. The model updates at the frequency of the MRMS radar data—about every 2 minutes.
When a storm develops and is tracked within satellite imagery, it has information about the storm environment from the RAP composite—which updates every hour. The probabilities are computed for every set of MRMS radar data—about every 2 minutes. The ENI total lightning data is also updated every 2 minutes. The update frequency of the current GOES satellite in routine scan mode is every 15 minutes, or roughly every 7.5 minutes in rapid-scan mode.
The critical point is:
The model does not wait on a satellite scan—it uses the most recent information available from satellite—whether the satellite is in routine scan mode or rapid scan mode. So users should expect updates in AWIPS-II about every 2 minutes.

## Slide 50
ProbSevere is being tested as automated probabilistic warning guidance in the PHI (Probabilistic Hazards Information) tool, a key component of FACETS.
Notes: We’re not doing this development in a vacuum. We’re using feedback from HWT forecasters, local PG experiments, leveraging research out of Boulder and Huntsville, AL, and we have a funded collaboration with some folks at NSSL in Norman. Forecasters at HWT were able to view these very experimental gridded threat swaths. So this is where warning operations is potentially headed.

## Slide 51: Take Away Points
Goal: ProbSevere is designed to support NWS severe weather warning operations. While skillful and getting better with additional research, ProbSevere will never fully replicate human expertise.
Current Primary Limitations: Linear convective modes can be under-forecast, pulse type convection can be over-forecast, downburst wind events tend to be under-forecast, no meaningful guidance when radar beam is significantly blocked by terrain, lead time is less when satellite does not contribute
Forthcoming Improvements: Hazard specific forecasts that will help mitigate many of the under and over forecasting issues
GOES-R Benefits: GOES-R will increase the skill and lead-time of ProbSevere guidance

## Slide 52
http://cimss.ssec.wisc.edu/severe_conv/probsev.html

## Slide 53: References
Pavolonis, M. J., 2010: Advances in Extracting Cloud Composition Information from Spaceborne Infrared Radiances-A Robust Alternative to Brightness Temperatures. Part I: Theory. Journal of Applied Meteorology and Climatology, 49, 1992-2012, doi:10.1175/2010JAMC2433.1 ER.
Cintineo, John L.; Pavolonis, Michael J.; Sieglaff, Justin M. and Heidinger, Andrew K. Evolution of severe and nonsevere convection inferred from GOES-derived cloud properties. Journal of Applied Meteorology and Climatology, 52 (9), 2013, 2009–2023.
Cintineo, John L.; Pavolonis, Michael J.; Sieglaff, Justin M. and Lindsey, Daniel T. An empirical model for assessing the severe weather potential of developing convection. Weather and Forecasting, 29 (3), 2014, 639–653.

## Slide 54: Additional Resources
Mike Pavolonis (michael.pavolonis@noaa.gov)
John Cintineo (john.cintineo@ssec.wisc.edu)
Justin Sieglaff (justin.sieglaff@ssec.wisc.edu)
Dan Lindsey (dan.lindsey@noaa.gov)
To access the official ProbSevere training module and supplemental training material:
http://cimss.ssec.wisc.edu/severe_conv/training/training.html
See ProbSevere blog posts:
http://goesrhwt.blogspot.com/search/label/ProbSevere

## Slide 55
Questions?

## Slide 57: Backup Slides

## Slide 58
https://www.youtube.com/watch?v=493mk5K1pO8
Local Media Coverage: Peoria, IL

## Slide 63: Reliability – Without Lightning
CAPE 1500-2500 J/Kg
CAPE 2500+ J/Kg
EBS 0-10 m/s
EBS 10-15 m/s
EBS 15+ m/s
Small Sample Size
Small Sample Size
CAPE 0-1500 J/Kg
Notes: Validation using ALL storm reports (not just the first)
total_sev_storms= 71 156 181 85 132 69 85 200 110 total_ns_storms= 8328 6667 6124 2090 1381 589 855 773 329

## Slide 64
CAPE 0-1500 J/Kg
CAPE 1500-2500 J/Kg
CAPE 2500+ J/Kg
EBS 0-10 m/s
EBS 10-15 m/s
EBS 15+ m/s
Small Sample Size
Small Sample Size
Reliability – With Lightning
Notes: Validation using ALL storm reports (not just the first)
total_sev_storms= 71 156 181 85 132 69 85 200 110 total_ns_storms= 8328 6667 6124 2090 1381 589 855 773 329