## Slide 1: Training on Polar Hyperspectral Soundings and Microwave Data and ABI modeling output
Bill Smith, Sr., Qi Zhang, Anthony diNorscia
Hampton University
Scott Lindstrom
University of Wisconsin/Madison CIMSS
Hazardous Weather Testbed May/June 2022

## Slide 2: PHSnMWnABI: That’s a mouthful!
I just call it PHS: Polar Hyperspectral Soundings
The Quickest explanation
  With each Polar Orbit, associations between JPSS data (infrared and Microwave) and ABI retrievals are established
  Those associations are stepped forward in time with each ABI scan, and used to initialize a numerical model each hour
  This method takes advantage of the excellent spectral resolution on LEO satellites, and the excellent spatial/temporal resolution on ABI

## Slide 3: Dual Regression Retrievals
Single field-of-view (FOV), all-sky condition, retrievals provide atmospheric soundings and surface and cloud parameters from hyperspectral sounders
  Hyperspectral data alone cannot tell you a value at a specific level – which is what you need for a numerical model
  Regression uses a model-based first guess field to sharpen the vertical resolution in the retrievals.
How does ABI data acquire better spectral resolution from Polar data?
How does Polar data acquire better spatial and temporal resolution from ABI?

## Slide 4: Flowchart that describes how ABI data acquires better spectral resolution
Start with ABI retrievals
Where do the ABI retrievals sit within the Polar footprint
Average all the ABI retrievals in the Polar Footprint
Find the 5 HiRes ABI retrievals that most closely match (in space and in profile T and RH!) the Low-Res (averaged) ABI retrievals
Average those 5 profiles together, note their location
The *Polar* Soundings for those 5 locations are also known.
PHSnABI is : HiResABI + (PHSavg – LowResABIAvg)

## Slide 5: How far into the future do these computed associations hold?
They don’t have to hold very long, because there are 4 Polar Orbiters being used.
  IASI from Metop (-B and –C) samples over CONUS ca. 01-04 and 14-17 UTC
  CrIS from Suomi-NPP/NOAA-20 samples over CONUS ca. 06-09 and 17-20 UTC
In practice, Polar data more than 7 hours old is not used.

## Slide 6: What’s the most important information?
Moisture
  Sounder information from CrIS (Suomi-NPP/NOAA-20) and IASI (MetOps) leads to a more accurate definition of the moisture distribution than might be occurring in the numerical model
Temperature
  Usually, temperature is well-forecast, so the additional temperature information from the polar orbiters is not quite so impactful as the moisture

## Slide 7: Which Satellites / When do they overfly?
Suomi NPP/NOAA-20 and Metop-B/Metop-C
What’s the maximum time between Polar overpasses: about 4-5 hours
Metop-C
Metop-B
NOAA20
0545
0555
0725
0735
0730
0915
0905
0910
S-NPP
1715
1855
1850
1710
0550
2035
2040
1945
1950
1800
1805
1755
0820
0815
0825
0645
0640
0635
1940
0250
0300
0245
1505
1650
1510
0255
1645
1555
1600
1735
1550
1415
1730
0155
0200
0340
0335
0345
Metop-B/Metop-C are paired
(one is in between the other)
Suomi-NPP/NOAA-20 are paired
(one is in between the other)

## Slide 8: Example over Florida: GOES-16 Vis/CAPE

## Slide 9: Example over Florida: GOES-16 Vis/PHS CAPE